## Slide 1: William Stallings Computer Organization and Architecture 10th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 10/e, by William Stallings, Chapter 7 “Input/Output”.

## Slide 2
Notes: The actual details of disk I/O operation depend on the computer system, the operating
system, and the nature of the I/O channel and disk controller hardware. A
general timing diagram of disk I/O transfer is shown in Figure 6.5.

## Slide 3: RAID
Consists of 7 levels
Levels do not imply a hierarchical relationship but designate different design architectures that share three common characteristics:
  Set of physical disk drives viewed by the operating system as a single logical drive
  Data are distributed across the physical drives of an array in a scheme known as striping
  Redundant disk capacity is used to store parity information, which guarantees data recoverability in case of a disk failure
Redundant Array of Independent Disks
Notes: With the use of multiple disks, there is a wide variety of ways in which the
data can be organized and in which redundancy can be added to improve reliability.
This could make it difficult to develop database schemes that are usable
on a number of platforms and operating systems. Fortunately, industry has
agreed on a standardized scheme for multiple-disk database design, known as
RAID (Redundant Array of Independent Disks). The RAID scheme consists
of seven levels, zero through six. These levels do not imply a hierarchical relationship
but designate different design architectures that share three common
characteristics:
1. RAID is a set of physical disk drives viewed by the operating system as a single
logical drive.
2. Data are distributed across the physical drives of an array in a scheme known
as striping, described subsequently.
3. Redundant disk capacity is used to store parity information, which guarantees
data recoverability in case of a disk failure.
The details of the second and third characteristics differ for the different RAID
levels. RAID 0 and RAID 1 do not support the third characteristic.
The term RAID was originally coined in a paper by a group of researchers
at the University of California at Berkeley [PATT88]. The paper outlined various
RAID configurations and applications and introduced the definitions of the
RAID levels that are still used. The RAID strategy employs multiple disk drives
and distributes data in such a way as to enable simultaneous access to data from
multiple drives, thereby improving I/O performance and allowing easier incremental
increases in capacity.

## Slide 4: Chapter 7
Input/Output
Notes: In addition to the processor and a set of memory modules, the third key element
of a computer system is a set of I/O modules. Each module interfaces to the system
bus or central switch and controls one or more peripheral devices. An I/O module
is not simply a set of mechanical connectors that wire a device into the system bus.
Rather, the I/O module contains logic for performing a communication function
between the peripheral and the bus.
The reader may wonder why one does not connect peripherals directly to the
system bus. The reasons are as follows:
• There are a wide variety of peripherals with various methods of operation. It
would be impractical to incorporate the necessary logic within the processor
to control a range of devices.
• The data transfer rate of peripherals is often much slower than that of the
memory or processor. Thus, it is impractical to use the high-speed system bus
to communicate directly with a peripheral.
• On the other hand, the data transfer rate of some peripherals is faster than
that of the memory or processor. Again, the mismatch would lead to inefficiencies
if not managed properly.
• Peripherals often use different data formats and word lengths than the
computer to which they are attached.

## Slide 5
Notes: Thus, an I/O module is required. This module has two major functions
(Figure 7.1):
• Interface to the processor and memory via the system bus or central switch
• Interface to one or more peripheral devices by tailored data links
We begin this chapter with a brief discussion of external devices, followed by
an overview of the structure and function of an I/O module. Then we look at the
various ways in which the I/O function can be performed in cooperation with the
processor and memory: the internal I/O interface. Finally, we examine the external
I/O interface, between the I/O module and the outside world.

## Slide 6
Notes: In very general terms, the nature of an external device is indicated in
Figure 7.2. The interface to the I/O module is in the form of control, data, and status
signals. Control signals determine the function that the device will perform, such as
send data to the I/O module (INPUT or READ), accept data from the I/O module
(OUTPUT or WRITE), report status, or perform some control function particular
to the device (e.g., position a disk head). Data are in the form of a set of bits to
be sent to or received from the I/O module. Status signals indicate the state of the
device. Examples are READY/NOT-READY to show whether the device is ready
for data transfer.
Control logic associated with the device controls the device’s operation in
response to direction from the I/O module. The transducer converts data from electrical
to other forms of energy during output and from other forms to electrical
during input. Typically, a buffer is associated with the transducer to temporarily
hold data being transferred between the I/O module and the external environment.
A buffer size of 8 to 16 bits is common for serial devices, whereas block-
oriented devices such as disk drive controllers may have much larger buffers.
The interface between the I/O module and the external device will be examined
in Section 7.7. The interface between the external device and the environment
is beyond the scope of this book, but several brief examples are given here.
A disk drive contains electronics for exchanging data, control, and status signals with
an I/O module plus the electronics for controlling the disk read/write mechanism.
In a fixed-head disk, the transducer is capable of converting between the magnetic
patterns on the moving disk surface and bits in the device’s buffer (Figure 7.2). A
Moving-head disk must also be able to cause the disk arm to move radially in and
out across the disk’s surface.

## Slide 7
Notes: I/O modules vary considerably in complexity and the number of external devices
that they control. We will attempt only a very general description here. (One specific
device, the Intel 82C55A, is described in Section 7.4.) Figure 7.3 provides a general
block diagram of an I/O module. The module connects to the rest of the computer
through a set of signal lines (e.g., system bus lines). Data transferred to and from the
module are buffered in one or more data registers. There may also be one or more
status registers that provide current status information. A status register may also
function as a control register, to accept detailed control information from the processor.
The logic within the module interacts with the processor via a set of control
lines. The processor uses the control lines to issue commands to the I/O module.
Some of the control lines may be used by the I/O module (e.g., for arbitration and
status signals). The module must also be able to recognize and generate addresses
associated with the devices it controls. Each I/O module has a unique address or, if
it controls more than one external device, a unique set of addresses. Finally, the I/O
module contains logic specific to the interface with each device that it controls.
An I/O module functions to allow the processor to view a wide range of devices
in a simple-minded way. There is a spectrum of capabilities that may be provided.
The I/O module may hide the details of timing, formats, and the electromechanics
of an external device so that the processor can function in terms of simple read and
write commands, and possibly open and close file commands. In its simplest form,
the I/O module may still leave much of the work of controlling a device (e.g., rewind
a tape) visible to the processor.
An I/O module that takes on most of the detailed processing burden, presenting
a high-level interface to the processor, is usually referred to as an I/O channel or
I/O processor. An I/O module that is quite primitive and requires detailed control
is usually referred to as an I/O controller or device controller. I/O controllers are
commonly seen on microcomputers, whereas I/O channels are used on mainframes.
In what follows, we will use the generic term I/O module when no confusion
results and will use more specific terms where necessary.

## Slide 8
Table 7.1
I/O Techniques
Notes: Table 7.1 indicates the relationship among these three techniques. In this section,
we explore programmed I/O. Interrupt I/O and DMA are explored in the following
two sections, respectively.

## Slide 9
Notes: Figure 7.4a gives an example of the use of programmed I/O to read in a block of
data from a peripheral device (e.g., a record from tape) into memory. Data are read
in one word (e.g., 16 bits) at a time. For each word that is read in, the processor must
remain in a status-checking cycle until it determines that the word is available in the
I/O module’s data register. This flowchart highlights the main disadvantage of this
technique: it is a time-consuming process that keeps the processor busy needlessly.

## Slide 10: I/O Instructions
With programmed I/O there is a close correspondence between the I/O-related instructions that the processor fetches from memory and the I/O commands that the processor issues to an I/O module to execute the instructions
The form of the instruction depends on the way in which external devices are addressed
Each I/O device connected through I/O modules is given a unique identifier or address
When the processor issues an I/O command, the command contains the address of the desired device
Thus each I/O module must interpret the address lines to determine if the command is for itself
Memory-mapped I/O
There is a single address space for memory locations and I/O devices
A single read line and a single write line are needed on the bus
Notes: With programmed I/O, there is a close correspondence between the I/O-related
instructions that the processor fetches from memory and the I/O commands that the
processor issues to an I/O module to execute the instructions. That is, the instructions
are easily mapped into I/O commands, and there is often a simple one-
to-one relationship. The form of the instruction depends on the way in which external
devices are addressed.
Typically, there will be many I/O devices connected through I/O modules to
the system. Each device is given a unique identifier or address. When the processor
issues an I/O command, the command contains the address of the desired device.
Thus, each I/O module must interpret the address lines to determine if the command
is for itself.
When the processor, main memory, and I/O share a common bus, two modes
of addressing are possible: memory mapped and isolated. With memory-mapped
I/O, there is a single address space for memory locations and I/O devices. The processor
treats the status and data registers of I/O modules as memory locations and
uses the same machine instructions to access both memory and I/O devices. So, for
example, with 10 address lines, a combined total of 210 = 1024 memory locations
and I/O addresses can be supported, in any combination.
With memory-mapped I/O, a single read line and a single write line are needed
on the bus. Alternatively, the bus may be equipped with memory read and write
plus input and output command lines. Now, the command line specifies whether the
address refers to a memory location or an I/O device. The full range of addresses
may be available for both. Again, with 10 address lines, the system may now support
both 1024 memory locations and 1024 I/O addresses. Because the address space for
I/O is isolated from that for memory, this is referred to as isolated I/O.

## Slide 11: Interrupt-Driven I/O
The problem with programmed I/O is that the processor has to wait a long time for the I/O module to be ready for either reception or transmission of data
An alternative is for the processor to issue an I/O command to a module and then go on to do some other useful work
The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor
The processor executes the data transfer and resumes its former processing
Notes: The problem with programmed I/O is that the processor has to wait a long time
for the I/O module of concern to be ready for either reception or transmission of
data. The processor, while waiting, must repeatedly interrogate the status of the I/O
module. As a result, the level of the performance of the entire system is severely
degraded.
An alternative is for the processor to issue an I/O command to a module and
then go on to do some other useful work. The I/O module will then interrupt the
processor to request service when it is ready to exchange data with the processor.
The processor then executes the data transfer, as before, and then resumes its
former processing.
Let us consider how this works, first from the point of view of the I/O module.
For input, the I/O module receives a READ command from the processor. The I/O
module then proceeds to read data in from an associated peripheral. Once the data
are in the module’s data register, the module signals an interrupt to the processor
over a control line. The module then waits until its data are requested by the processor.
When the request is made, the module places its data on the data bus and is
then ready for another I/O operation.
From the processor’s point of view, the action for input is as follows. The processor
issues a READ command. It then goes off and does something else (e.g., the
processor may be working on several different programs at the same time). At the
end of each instruction cycle, the processor checks for interrupts (Figure 3.9). When
the interrupt from the I/O module occurs, the processor saves the context (e.g., program
counter and processor registers) of the current program and processes the
interrupt. In this case, the processor reads the word of data from the I/O module
and stores it in memory. It then restores the context of the program it was working
on (or some other program) and resumes execution.
Figure 7.4b shows the use of interrupt I/O for reading in a block of data.
Compare this with Figure 7.4a. Interrupt I/O is more efficient than programmed I/O
because it eliminates needless waiting. However, interrupt I/O still consumes a lot of
processor time, because every word of data that goes from memory to I/O module
or from I/O module to memory must pass through the processor.

## Slide 12
Notes: Let us consider the role of the processor in interrupt-driven I/O in more detail.
The occurrence of an interrupt triggers a number of events, both in the processor
hardware and in software. Figure 7.6 shows a typical sequence. When an I/O device
completes an I/O operation, the following sequence of hardware events occurs:
1. The device issues an interrupt signal to the processor.
2. The processor finishes execution of the current instruction before responding
to the interrupt, as indicated in Figure 3.9.
3. The processor tests for an interrupt, determines that there is one, and sends an
acknowledgment signal to the device that issued the interrupt. The acknowledgment
allows the device to remove its interrupt signal.
4. The processor now needs to prepare to transfer control to the interrupt routine.
To begin, it needs to save information needed to resume the current program at
the point of interrupt. The minimum information required is (a) the status of the
processor, which is contained in a register called the program status word (PSW),
and (b) the location of the next instruction to be executed, which is contained in
the program counter. These can be pushed onto the system control stack.
5. The processor now loads the program counter with the entry location of the
interrupt-handling program that will respond to this interrupt. Depending on
the computer architecture and operating system design, there may be a single
program; one program for each type of interrupt; or one program for each
device and each type of interrupt. If there is more than one interrupt-handling
routine, the processor must determine which one to invoke. This information
may have been included in the original interrupt signal, or the processor may
have to issue a request to the device that issued the interrupt to get a response
that contains the needed information.

## Slide 13
Notes: Once the program counter has been loaded, the processor proceeds to the
next instruction cycle, which begins with an instruction fetch. Because the instruction
fetch is determined by the contents of the program counter, the result is that
control is transferred to the interrupt-handler program. The execution of this program
results in the following operations:
6. At this point, the program counter and PSW relating to the interrupted
program have been saved on the system stack. However, there is other information
that is considered part of the “state” of the executing program. In particular,
the contents of the processor registers need to be saved, because these
registers may be used by the interrupt handler. So, all of these values, plus any
other state information, need to be saved. Typically, the interrupt handler will
begin by saving the contents of all registers on the stack. Figure 7.7a shows a
simple example. In this case, a user program is interrupted after the instruction
at location N. The contents of all of the registers plus the address of the next
instruction (N + 1) are pushed onto the stack. The stack pointer is updated to
point to the new top of stack, and the program counter is updated to point to
the beginning of the interrupt service routine.
7. The interrupt handler next processes the interrupt. This includes an examination
of status information relating to the I/O operation or other event that
caused an interrupt. It may also involve sending additional commands or
acknowledgments to the I/O device.
8. When interrupt processing is complete, the saved register values are retrieved
from the stack and restored to the registers (e.g., see Figure 7.7b).
9. The final act is to restore the PSW and program counter values from the stack.
As a result, the next instruction to be executed will be from the previously
interrupted program.
Note that it is important to save all the state information about the interrupted
program for later resumption. This is because the interrupt is not a routine called
from the program. Rather, the interrupt can occur at any time and therefore at any
point in the execution of a user program. Its occurrence is unpredictable. Indeed, as
we will see in the next chapter, the two programs may not have anything in common
and may belong to two different users.

## Slide 14: Design Issues
Two design issues arise in implementing interrupt I/O:
Because there will be multiple I/O modules how does the processor determine which device issued the interrupt?
If multiple interrupts have occurred how does the processor decide which one to process?
Notes: Two design issues arise in implementing interrupt I/O. First, because there will
almost invariably be multiple I/O modules, how does the processor determine which
device issued the interrupt? And second, if multiple interrupts have occurred, how
does the processor decide which one to process?

## Slide 15: Device Identification
  Multiple interrupt lines
  Between the processor and the I/O modules
  Most straightforward approach to the problem
  Consequently even if multiple lines are used, it is likely that each line will have multiple I/O modules attached to it
  Software poll
  When processor detects an interrupt it branches to an interrupt-service routine whose job is to poll each I/O module to determine which module caused the interrupt
  Time consuming
  Daisy chain (hardware poll, vectored)
  The interrupt acknowledge line is daisy chained through the modules
  Vector – address of the I/O module or some other unique identifier
  Vectored interrupt – processor uses the vector as a pointer to the appropriate device-service routine, avoiding the need to execute a general interrupt-service routine first
  Bus arbitration (vectored)
  An I/O module must first gain control of the bus before it can raise the interrupt request line
  When the processor detects the interrupt it responds on the interrupt acknowledge line
  Then the requesting module places its vector on the data lines
Four general categories of techniques are in common use:
Notes: Let us consider device identification first. Four general categories of techniques
are in common use:
• Multiple interrupt lines
• Software poll
• Daisy chain (hardware poll, vectored)
• Bus arbitration (vectored)
The most straightforward approach to the problem is to provide multiple interrupt
lines between the processor and the I/O modules. However, it is impractical to
dedicate more than a few bus lines or processor pins to interrupt lines. Consequently,
even if multiple lines are used, it is likely that each line will have multiple I/O modules
attached to it. Thus, one of the other three techniques must be used on each line.
One alternative is the software poll. When the processor detects an interrupt,
it branches to an interrupt-service routine whose job it is to poll each I/O module
to determine which module caused the interrupt. The poll could be in the form of a
separate command line (e.g., TESTI/O). In this case, the processor raises TESTI/O
and places the address of a particular I/O module on the address lines. The I/O module
responds positively if it sets the interrupt. Alternatively, each I/O module could
contain an addressable status register. The processor then reads the status register
of each I/O module to identify the interrupting module. Once the correct module is
identified, the processor branches to a device-service routine specific to that device.
The disadvantage of the software poll is that it is time consuming. A more efficient
technique is to use a daisy chain, which provides, in effect, a hardware poll. An example
of a daisy-chain configuration is shown in Figure 3.26. For interrupts, all I/O modules
share a common interrupt request line. The interrupt acknowledge line is daisy chained
through the modules. When the processor senses an interrupt, it sends out an interrupt
acknowledge. This signal propagates through a series of I/O modules until it gets to a
requesting module. The requesting module typically responds by placing a word on
the data lines. This word is referred to as a vector and is either the address of the I/O
module or some other unique identifier. In either case, the processor uses the vector as
a pointer to the appropriate device-service routine. This avoids the need to execute a
general interrupt-service routine first. This technique is called a vectored interrupt.
There is another technique that makes use of vectored interrupts, and that is
bus arbitration. With bus arbitration, an I/O module must first gain control of the
bus before it can raise the interrupt request line. Thus, only one module can raise the
line at a time. When the processor detects the interrupt, it responds on the interrupt
acknowledge line. The requesting module then places its vector on the data lines.

## Slide 16: Device Identification
  Daisy chain (hardware poll, vectored)
  The interrupt acknowledge line is daisy chained through the modules
  Vector – address of the I/O module or some other unique identifier
  Vectored interrupt – processor uses the vector as a pointer to the appropriate device-service routine, avoiding the need to execute a general interrupt-service routine first
Interrupt vector
table
Interrupt service routine1
Interrupt service routine2
Interrupt service routine3
Notes: Let us consider device identification first. Four general categories of techniques
are in common use:
• Multiple interrupt lines
• Software poll
• Daisy chain (hardware poll, vectored)
• Bus arbitration (vectored)
The most straightforward approach to the problem is to provide multiple interrupt
lines between the processor and the I/O modules. However, it is impractical to
dedicate more than a few bus lines or processor pins to interrupt lines. Consequently,
even if multiple lines are used, it is likely that each line will have multiple I/O modules
attached to it. Thus, one of the other three techniques must be used on each line.
One alternative is the software poll. When the processor detects an interrupt,
it branches to an interrupt-service routine whose job it is to poll each I/O module
to determine which module caused the interrupt. The poll could be in the form of a
separate command line (e.g., TESTI/O). In this case, the processor raises TESTI/O
and places the address of a particular I/O module on the address lines. The I/O module
responds positively if it sets the interrupt. Alternatively, each I/O module could
contain an addressable status register. The processor then reads the status register
of each I/O module to identify the interrupting module. Once the correct module is
identified, the processor branches to a device-service routine specific to that device.
The disadvantage of the software poll is that it is time consuming. A more efficient
technique is to use a daisy chain, which provides, in effect, a hardware poll. An example
of a daisy-chain configuration is shown in Figure 3.26. For interrupts, all I/O modules
share a common interrupt request line. The interrupt acknowledge line is daisy chained
through the modules. When the processor senses an interrupt, it sends out an interrupt
acknowledge. This signal propagates through a series of I/O modules until it gets to a
requesting module. The requesting module typically responds by placing a word on
the data lines. This word is referred to as a vector and is either the address of the I/O
module or some other unique identifier. In either case, the processor uses the vector as
a pointer to the appropriate device-service routine. This avoids the need to execute a
general interrupt-service routine first. This technique is called a vectored interrupt.
There is another technique that makes use of vectored interrupts, and that is
bus arbitration. With bus arbitration, an I/O module must first gain control of the
bus before it can raise the interrupt request line. Thus, only one module can raise the
line at a time. When the processor detects the interrupt, it responds on the interrupt
acknowledge line. The requesting module then places its vector on the data lines.

## Slide 17: Drawbacks of Programmed and Interrupt-Driven I/O
Both forms of I/O suffer from two inherent drawbacks:
  The I/O transfer rate is limited by the speed with which the processor can test and service a device
  The processor is tied up in managing an I/O transfer; a number of instructions must be executed for each I/O transfer
When large volumes of data are to be moved a more efficient technique is direct memory access (DMA)
Notes: Interrupt-driven I/O, though more efficient than simple programmed I/O, still
requires the active intervention of the processor to transfer data between memory
and an I/O module, and any data transfer must traverse a path through the processor.
Thus, both these forms of I/O suffer from two inherent drawbacks:
1. The I/O transfer rate is limited by the speed with which the processor can test
and service a device.
2. The processor is tied up in managing an I/O transfer; a number of instructions
must be executed for each I/O transfer (e.g., Figure 7.5).
There is somewhat of a trade-off between these two drawbacks. Consider the
transfer of a block of data. Using simple programmed I/O, the processor is dedicated
to the task of I/O and can move data at a rather high rate, at the cost of doing
nothing else. Interrupt I/O frees up the processor to some extent at the expense of
the I/O transfer rate. Nevertheless, both methods have an adverse impact on both
processor activity and I/O transfer rate.
When large volumes of data are to be moved, a more efficient technique is
required: direct memory access (DMA).

## Slide 18
Notes: Figure 7.13 shows where in the instruction cycle the processor may be suspended.
In each case, the processor is suspended just before it needs to use the bus.
The DMA module then transfers one word and returns control to the processor.
Note that this is not an interrupt; the processor does not save a context and do
something else. Rather, the processor pauses for one bus cycle. The overall effect
is to cause the processor to execute more slowly. Nevertheless, for a multiple-word
I/O transfer, DMA is far more efficient than interrupt-driven or programmed I/O.

## Slide 19
Notes: The DMA mechanism can be configured in a variety of ways. Some possibilities
are shown in Figure 7.14. In the first example, all modules share the same system
bus. The DMA module, acting as a surrogate processor, uses programmed I/O to
exchange data between memory and an I/O module through the DMA module. This
configuration, while it may be inexpensive, is clearly inefficient. As with processor controlled
programmed I/O, each transfer of a word consumes two bus cycles.
The number of required bus cycles can be cut substantially by integrating the
DMA and I/O functions. As Figure 7.14b indicates, this means that there is a path
between the DMA module and one or more I/O modules that does not include the
system bus. The DMA logic may actually be a part of an I/O module, or it may be a
separate module that controls one or more I/O modules. This concept can be taken
one step further by connecting I/O modules to the DMA module using an I/O bus
(Figure 7.14c). This reduces the number of I/O interfaces in the DMA module to one
and provides for an easily expandable configuration. In both of these cases (Figures
7.14b and c), the system bus that the DMA module shares with the processor and
memory is used by the DMA module only to exchange data with memory. The
exchange of data between the DMA and I/O modules takes place off the system
bus.

## Slide 20
Notes: The Intel 8237A DMA controller interfaces to the 80 x 86 family of processors and
to DRAM memory to provide a DMA capability. Figure 7.15 indicates the location
of the DMA module. When the DMA module needs to use the system buses (data,
address, and control) to transfer data, it sends a signal called HOLD to the processor.
The processor responds with the HLDA (hold acknowledge) signal, indicating
that the DMA module can use the buses. For example, if the DMA module is to
transfer a block of data from memory to disk, it will do the following:
1. The peripheral device (such as the disk controller) will request the service of
DMA by pulling DREQ (DMA request) high.
2. The DMA will put a high on its HRQ (hold request), signaling the CPU
through its HOLD pin that it needs to use the buses.
3.The CPU will finish the present bus cycle (not necessarily the present instruction)
and respond to the DMA request by putting high on its HDLA (hold
acknowledge), thus telling the 8237 DMA that it can go ahead and use the
buses to perform its task. HOLD must remain active high as long as DMA is
performing its task.
4. DMA will activate DACK (DMA acknowledge), which tells the peripheral
device that it will start to transfer the data.
5. DMA starts to transfer the data from memory to peripheral by putting the
address of the first byte of the block on the address bus and activating MEMR,
thereby reading the byte from memory into the data bus; it then activates IOW
to write it to the peripheral. Then DMA decrements the counter and increments
the address pointer and repeats this process until the count reaches zero
and the task is finished.
6. After the DMA has finished its job it will deactivate HRQ, signaling the CPU
that it can regain control over its buses.

## Slide 21: Evolution of the I/O Function
The CPU directly controls a peripheral device.
A controller or I/O module is added. The CPU uses programmed I/O without interrupts.
Same configuration as in step 2 is used, but now interrupts are employed. The CPU need not spend time waiting for an I/O operation to be performed, thus increasing efficiency.
The I/O module is given direct access to memory via DMA. It can now move a block of data to or from memory without involving the CPU, except at the beginning and end of the transfer.
The I/O module is enhanced to become a processor in its own right, with a specialized instruction set tailored for I/O
The I/O module has a local memory of its own and is, in fact, a computer in its own right. With this architecture a large set of I/O devices can be controlled with minimal CPU involvement.
Notes: As computer systems have evolved, there has been a pattern of increasing complexity
and sophistication of individual components. Nowhere is this more evident than
in the I/O function. We have already seen part of that evolution. The evolutionary
steps can be summarized as follows:
1. The CPU directly controls a peripheral device. This is seen in simple microprocessor-
controlled devices.
2. A controller or I/O module is added. The CPU uses programmed I/O without
interrupts. With this step, the CPU becomes somewhat divorced from the specific
details of external device interfaces.
3. The same configuration as in step 2 is used, but now interrupts are employed.
The CPU need not spend time waiting for an I/O operation to be performed,
thus increasing efficiency.
4. The I/O module is given direct access to memory via DMA. It can now move
a block of data to or from memory without involving the CPU, except at the
beginning and end of the transfer.
5. The I/O module is enhanced to become a processor in its own right, with a
specialized instruction set tailored for I/O. The CPU directs the I/O processor
to execute an I/O program in memory. The I/O processor fetches and executes
these instructions without CPU intervention. This allows the CPU to specify a
sequence of I/O activities and to be interrupted only when the entire sequence
has been performed.
6. The I/O module has a local memory of its own and is, in fact, a computer
in its own right. With this architecture, a large set of I/O devices can be
controlled, with minimal CPU involvement. A common use for such an
architecture has been to control communication with interactive terminals.
The I/O processor takes care of most of the tasks involved in controlling the
terminals.
As one proceeds along this evolutionary path, more and more of the I/O
function is performed without CPU involvement. The CPU is increasingly
relieved of I/O-related tasks, improving performance. With the last two steps
(5–6), a major change occurs with the introduction of the concept of an I/O module
capable of executing a program. For step 5, the I/O module is often referred
to as an I/O channel. For step 6, the term I/O processor is often used. However,
both terms are on occasion applied to both situations. In what follows, we will use
the term I/O channel.

## Slide 22
Notes: The I/O channel represents an extension of the DMA concept. An I/O
channel has the ability to execute I/O instructions, which gives it complete control
over I/O operations. In a computer system with such devices, the CPU does
not execute I/O instructions. Such instructions are stored in main memory to
be executed by a special-purpose processor in the I/O channel itself. Thus, the
CPU initiates an I/O transfer by instructing the I/O channel to execute a program
in memory. The program will specify the device or devices, the area or
areas of memory for storage, priority, and actions to be taken for certain error
conditions. The I/O channel follows these instructions and controls the data
transfer.
Two types of I/O channels are common, as illustrated in Figure 7.18. A
selector channel controls multiple high-speed devices and, at any one time, is
dedicated to the transfer of data with one of those devices. Thus, the I/O channel
selects one device and effects the data transfer. Each device, or a small set of
devices, is handled by a controller, or I/O module, that is much like the I/O modules
we have been discussing. Thus, the I/O channel serves in place of the CPU in
controlling these I/O controllers. A multiplexor channel can handle I/O with multiple
devices at the same time. For low-speed devices, a byte multiplexor accepts or
transmits characters as fast as possible to multiple devices. For example, the resultant
character stream from three devices with different rates and individual streams
A1A2A3A4 …, B1B2B3B4 …, and C1C2C3C4 … might be A1B1C1A2C2A3B2C3A4,
and so on. For high-speed devices, a block multiplexor interleaves blocks of data
from several devices.

## Slide 23: Universal Serial Bus (USB)
Widely used for peripheral connections
Is the default interface for slower speed devices
Commonly used high-speed I/O
Has gone through multiple generations
  USB 1.0
    Defined a Low Speed data rate of 1.5 Mbps and a Full Speed rate of 12 Mbps
  USB 2.0
    Provides a data rate of 480 Mbps
  USB 3.0
    Higher speed bus called SuperSpeed in parallel with the USB 2.0 bus
    Signaling speed of SuperSpeed is 5 Gbps, but due to signaling overhead the usable data rate is up to 4 Gbps
  USB 3.1
    Includes a faster transfer mode called SuperSpeed+
    This transfer mode achieves a signaling rate of 10 Gbps and a theoretical usable data rate of 9.7 Gbps
Is controlled by a root host controller which attaches to devices to create a local network with a hierarchical tree topology
Notes: USB is widely used for peripheral connections. It is the default interface for slower
speed devices, such as keyboard and pointing devices, but is also commonly used for
high-speed I/O, including printers, disk drives, and network adapters.
USB has gone through multiple generations. The first version, USB 1.0,
defined a Low Speed data rate of 1.5 Mbps and a Full Speed rate of 12 Mbps. USB
2.0 provides a data rate of 480 Mbps. USB 3.0 includes a new, higher speed bus
called SuperSpeed in parallel with the USB 2.0 bus. The signaling speed of Super-
Speed is 5 Gbps, but due to signaling overhead, the usable data rate is up to 4 Gbps.
The most recent specification is USB 3.1, which includes a faster transfer mode
called SuperSpeed+ . This transfer mode achieves a signaling rate of 10 Gbps and a
theoretical usable data rate of 9.7 Gbps.
A USB system is controlled by a root host controller, which attaches to devices
to create a local network with a hierarchical tree topology.

## Slide 24: FireWire Serial Bus
Was developed as an alternative to small computer system interface (SCSI) to be used on smaller systems, such as personal computers, workstations, and servers
Objective was to meet the increasing demands for high I/O rates while avoiding the bulky and expensive I/O channel technologies developed for mainframe and supercomputer systems
IEEE standard 1394, for a High Performance Serial Bus
Uses a daisy chain configuration, with up to 63 devices connected off a single port
1022 FireWire buses can be interconnected using bridges
Provides for hot plugging which makes it possible to connect and disconnect peripherals without having to power the computer system down or reconfigure the system
Provides for automatic configuration
No terminations and the system automatically performs a configuration function to assign addresses
Notes: FireWire was developed as an alternative to small computer system interface (SCSI)
to be used on smaller systems, such as personal computers, workstations, and servers.
The objective was to meet the increasing demands for high I/O rates on these systems,
while avoiding the bulky and expensive I/O channel technologies developed
for mainframe and supercomputer systems. The result is the IEEE standard 1394, for
a High Performance Serial Bus, commonly known as FireWire.
FireWire uses a daisy-chain configuration, with up to 63 devices connected
off a single port. Moreover, up to 1022 FireWire buses can be interconnected using
bridges, enabling a system to support as many peripherals as required.
FireWire provides for what is known as hot plugging, which makes it possible
to connect and disconnect peripherals without having to power the computer system
down or reconfigure the system. Also, FireWire provides for automatic configuration;
it is not necessary manually to set device IDs or to be concerned with the relative
position of devices. With FireWire, there are no terminations, and the system
automatically performs a configuration function to assign addresses. A FireWire bus
need not be a strict daisy chain. Rather, a tree-structured configuration is possible.
An important feature of the FireWire standard is that it specifies a set of three
layers of protocols to standardize the way in which the host system interacts with the
peripheral devices over the serial bus. The physical layer defines the transmission media
that are permissible under FireWire and the electrical and signaling characteristics of
each. Data rates from 25 Mbps to 3.2 Gbps are defined. The link layer describes the
transmission of data in the packets. The transaction layer defines a request–
response protocol that hides the lower-layer details of FireWire from applications.

## Slide 25: SCSI
Small Computer System Interface
A once common standard for connecting peripheral devices to small and medium-sized computers
Has lost popularity to USB and FireWire in smaller systems
High-speed versions remain popular for mass memory support on enterprise systems
Physical organization is a shared bus, which can support up to 16 or 32 devices, depending on the generation of the standard
  The bus provides for parallel transmission rather than serial, with a bus width of 16 bits on earlier generations and 32 bits on later generations
  Speeds range from 5 Mbps on the original SCSI-1 specification to 160 Mbps on SCSI-3 U3
Notes: SCSI is a once common standard for connecting peripheral devices (disks, modems,
printers, etc.) to small and medium-sized computers. Although SCSI has evolved to
higher data rates, it has lost popularity to such competitors as USB and FireWire
in smaller systems. However, high-speed versions of SCSI remain popular for mass
memory support on enterprise systems. For example, the IBM zEnterprise EC12
and other IBM mainframes offer support for SCSI, and a number of Seagate hard
drive systems use SCSI.
The physical organization of SCSI is a shared bus, which can support up to 16
or 32 devices, depending on the generation of the standard. The bus provides for
parallel transmission rather than serial, with a bus width of 16 bits on earlier generations
and 32 bits on later generations. Speeds range from 5 Mbps on the original
SCSI-1 specification to 160 Mbps on SCSI-3 U3.

## Slide 26: InfiniBand
I/O specification aimed at the high-end server market
First version was released in early 2001
Heavily relied on by IBM zEnterprise series of mainframes
Standard describes an architecture and specifications for data flow among processors and intelligent I/O devices
Has become a popular interface for storage area networking and other large storage configurations
Enables servers, remote storage, and other network devices to be attached in a central fabric of switches and links
The switch-based architecture can connect up to 64,000 servers, storage systems, and networking devices
Notes: InfiniBand is an I/O specification aimed at the high-end server market. The first
version of the specification was released in early 2001 and has attracted numerous
vendors. For example, IBM zEnterprise series of mainframes has relied heavily on
InfiniBand for a number of years. The standard describes an architecture and specifications
for data flow among processors and intelligent I/O devices. InfiniBand has
become a popular interface for storage area networking and other large storage configurations.
In essence, InfiniBand enables servers, remote storage, and other network
devices to be attached in a central fabric of switches and links. The switch-based
architecture can connect up to 64,000 servers, storage systems, and networking devices.
Infiniband is described in detail in Appendix J.

## Slide 27
High-speed bus system for connecting peripherals of a wide variety of types and speeds
Serial Advanced Technology Attachment
An interface for disk storage systems
Provides data rates of up to 6 Gbps, with a maximum per device of 300 Mbps
Widely used in desktop computers and in industrial and embedded applications
PCI Express
SATA
Notes: PCI Express is a high-speed
bus system for connecting peripherals of a wide variety
of types and speeds. Chapter 3 discusses PCI Express in detail.
Serial ATA (Serial Advanced Technology Attachment) is an interface for disk storage
systems. It provides data rates of up to 6 Gbps, with a maximum per device of
300 Mbps. SATA is widely used in desktop computers, and in industrial and embedded
applications.

## Slide 28: Ethernet
Predominant wired networking technology
Has evolved to support data rates up to 100 Gbps and distances from a few meters to tens of km
Has become essential for supporting personal computers, workstations, servers, and massive data storage devices in organizations large and small
Began as an experimental bus-based 3-Mbps system
Has moved from bus-based to switch-based
  Data rate has periodically increased by an order of magnitude
  There is a central switch with all of the devices connected directly to the switch
  Ethernet systems are currently available at speeds up to 100 Gbps
Notes: Ethernet is the predominant wired networking technology, used in homes, offices,
data centers, enterprises, and wide-area networks. As Ethernet has evolved to support
data rates up to 100 Gbps and distances from a few meters to tens of km, it
has become essential for supporting personal computers, workstations, servers, and
massive data storage devices in organizations large and small.
Ethernet began as an experimental bus-based 3-Mbps system. With a bus system,
all of the attached devices, such as PCs, connect to a common coaxial cable,
much like residential cable TV systems. The first commercially-available Ethernet,
and the first version of IEEE 802.3, were bus-based systems operating at 10
Mbps. As technology has advanced, Ethernet has moved from bus-based
to switch-based, and the data rate has periodically increased by an order of magnitude. With
switch-based systems, there is a central switch, with all of the devices connected
directly to the switch. Currently, Ethernet systems are available at speeds up to 100
Gbps. Here’s a brief chronology.
■ 1983: 10 Mbps (megabit per second, million bits per second)
■ 1995: 100 Mbps
■ 1998: 1 Gbps (gigabit per second, billion bits per second)
■ 2003: 10 Gbps
■ 2010: 40 Gbps and 100 Gbps

## Slide 29: Wi-Fi
Is the predominant wireless Internet access technology
Now connects computers, tablets, smart phones, and other electronic devices such as video cameras TVs and thermostats
In the enterprise has become an essential means of enhancing worker productivity and network effectiveness
Public hotspots have expanded dramatically to provide free Internet access in most public places
As the technology of antennas, wireless transmission techniques, and wireless protocol design has evolved, the IEEE 802.11 committee has been able to introduce standards for new versions of Wi-Fi at higher speeds
  Current version is 802.11ac (2014) with a maximum data rate of 3.2 Gbps
Notes: Wi-Fi is the predominant wireless Internet access technology, used in homes, offices,
and public spaces. Wi-Fi in the home now connects computers, tablets, smart phones,
and a host of electronic devices, such as video cameras, TVs, and thermostats. Wi-Fi
in the enterprise has become an essential means of enhancing worker productivity
and network effectiveness. And public Wi-Fi hotspots have expanded dramatically
to provide free Internet access in most public places.
As the technology of antennas, wireless transmission techniques, and wireless
protocol design has evolved, the IEEE 802.11 committee has been able to introduce
standards for new versions of Wi-Fi at ever-higher speeds. Once the standard is
issued, industry quickly develops the products. Here’s a brief chronology, starting
with the original standard, which was simply called IEEE 802.11, and showing the
maximum data rate for each version:
■ 802.11 (1997): 2 Mbps (megabit per second, million bits per second)
■ 802.11a (1999): 54 Mbps
■ 802.11b (1999): 11 Mbps
■ 802.11n (1999): 600 Mbps
■ 802.11g (2003): 54 Mbps
■ 802.11ad (2012): 6.76 Gbps (billion bits per second)
■ 802.11ac (2014): 3.2 Gbps

## Slide 30: Summary
External devices
  Keyboard/monitor
  Disk drive
I/O modules
  Module function
  I/O module structure
Programmed I/O
  Overview of programmed I/O
  I/O commands/instructions
  Direct memory access
  Drawbacks of programmed and interrupt-driven I/O
  DMA function
  Intel 8237A DMA controller
Interrupt-driven I/O
  Interrupt processing
  Design issues
  Intel 82C59A interrupt controller
  Intel 82C55A programmable peripheral interface
  Direct Cache Access
  DMA using shared last-level cache
  Cache-related performance issues
  Direct cache access strategies
  Direct data I/O
  I/O channels and processors
  The evolution of the I/O function
  Characteristics of I/O channels
Chapter 7
Input/Output
Notes: Chapter 7 summary.

## Slide 31: Assignment 2.(과제2)
1. Explain the locality of memory reference and explain the hierarchical memory system.
2. Main memory:16GB(Ta=45ns), Block:16Bytes, Cache: 16MB(Ta=5ns)
1) What is the number of address bits connected to the main memory? (Assume byte addressable)
2) Show the size of the Tag in case of Direct Mapping and Associative Mapping.
3) Show the advantage(s) of associative mapping over direct mapping.
4) Explain a mapping method which does not require replacement algorithm.
5) If the given main memory is implemented with 4G×1bit memory chips, how many memory chips are needed?
6) Determine the cache hit ratio for the effective memory access time of 10ns.
3. Explain the case when write through policy is better than write back policy?
4. Explain advantages of a split cache compared to a unified cache.
5. Select all volatile memories. ① SDRAM ② Flash memory ③ SSD ④ CD-R ⑤ Hard disk ⑥ SRAM ⑦ EEPROM ⑧ DDR SDRAM
6. What is the major advantage of interrupt-driven IO over programmed IO?
7. Explain how an external device indicates an Interrupt event to the processor and how the processor identifies the external device.