## Slide 1: William Stallings Computer Organization and Architecture 10th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 10/e, by William Stallings, Chapter 2 “Performance Issues”.

## Slide 2: Structure
Notes: We now look in a general way at the internal structure of a computer. We begin with
a traditional computer with a single processor that employs a microprogrammed
control unit, then examine a typical multicore structure.
Figure 1.1 provides a hierarchical view
of the internal structure of a traditional single-processor computer.

## Slide 3: Table 1.2 Computer Generations
Notes: It has become widely accepted to classify computers into generations based on the fundamental
hardware technology employed (Table 1.2). Each new generation is characterized
by greater processing performance, larger memory capacity, and smaller
size than the previous one.

## Slide 4
Notes: Figure 1.6 shows the general structure of the IAS computer (compare with Figure 1.1).
It consists of
• A main memory, which stores both data and instructions
• An arithmetic and logic unit (ALU) capable of operating on binary data
• A control unit, which interprets the instructions in memory and causes them
to be executed
• Input/output (I/O) equipment operated by the control unit
This structure was outlined in von Neumann’s earlier proposal, which is worth
quoting in part at this point [VONN45]:
2.2 First: Since the device is primarily a computer, it will
have to perform the elementary operations of arithmetic most frequently.
These are addition, subtraction, multiplication, and division.
It is therefore reasonable that it should contain specialized
organs for just these operations.
It must be observed, however, that while this principle as such
is probably sound, the specific way in which it is realized requires
close scrutiny. At any rate a central arithmetical part of the device will
probably have to exist, and this constitutes the first specific part: CA .
2.3 Second: The logical control of the device, that is, the
proper sequencing of its operations, can be most efficiently carried
out by a central control organ. If the device is to be elastic ,
that is, as nearly as possible all purpose , then a distinction must
be made between the specific instructions given for and defining
a particular problem, and the general control organs that see to it
that these instructions—no matter what they are—are
carried out. The former must be stored in some way; the latter are represented
by definite operating parts of the device. By the central control we
mean this latter function only, and the organs that perform it form
the second specific part: CC .
2.4 Third: Any device that is to carry out long and complicated
sequences of operations (specifically of calculations) must
have a considerable memory . . .
The instructions which govern a complicated problem may
constitute considerable material, particularly so, if the code is circumstantial
(which it is in most arrangements). This material must
be remembered.
At any rate, the total memory constitutes the third specific
part of the device: M.
2.6 The three specific parts CA, CC (together C), and M correspond
to the associative neurons in the human nervous system. It
remains to discuss the equivalents of the sensory or afferent and the
motor or efferent neurons. These are the input and output organs of
the device. The device must be endowed with the ability to maintain
input and output (sensory and motor) contact with some specific
medium of this type. The medium will be called the outside recording
medium of the device: R .
2.7 Fourth: The device must have organs to transfer information
from R into its specific parts C and M. These organs form its
input , the fourth specific part: I . It will be seen that it is best to make
all transfers from R (by I) into M and never directly from C.
2.8 Fifth: The device must have organs to transfer from its
specific parts C and M into R. These organs form its output , the
fifth specific part: O . It will be seen that it is again best to make all
transfers from M (by O) into R, and never directly from C.

## Slide 5
Notes: With rare exceptions, all of today’s computers have this same general structure
and function and are thus referred to as von Neumann machines . Thus, it is worthwhile
at this point to describe briefly the operation of the IAS computer [BURK46,
GOLD54]. Following [HAYE98], the terminology and notation of von Neumann
are changed in the following to conform more closely to modern usage; the examples
accompanying this discussion are based on that latter text.
The memory of the IAS consists of 4,096 storage locations, called words , of
40 binary digits (bits) each.6 Both data and instructions are stored there. Numbers are
represented in binary form, and each instruction is a binary code. Figure 1.7 illustrates
these formats. Each number is represented by a sign bit and a 39-bit value. A word
may alternatively contain two 20-bit instructions, with each instruction consisting
of an 8-bit operation code (opcode ) specifying the operation to be performed and
a 12-bit address designating one of the words in memory (numbered from 0 to 999).

## Slide 6: Registers
Memory buffer register (MBR)
Contains a word to be stored in memory or sent to the I/O unit
Or is used to receive a word from memory or from the I/O unit
Memory address register (MAR)
Specifies the address in memory of the word to be written from or read into the MBR
Instruction register (IR)
Contains the 8-bit opcode instruction being executed
Instruction buffer register (IBR)
Employed to temporarily hold the right-hand instruction from a word in memory
Program counter (PC)
Contains the address of the next instruction pair to be fetched from memory
Accumulator (AC) and multiplier quotient (MQ)
Employed to temporarily hold operands and results of ALU operations
Notes: The control unit operates the IAS by fetching instructions from memory
and executing them one at a time. We explain these operations with reference to
Figure 1.6. This figure reveals that both the control unit and the ALU contain storage
locations, called registers , defined as follows:
Memory buffer register (MBR): Contains a word to be stored in memory or sent
to the I/O unit, or is used to receive a word from memory or from the I/O unit.
• Memory address register (MAR): Specifies the address in memory of the word
to be written from or read into the MBR.
• Instruction register (IR ): Contains the 8-bit opcode instruction being executed.
• Instruction buffer register (IBR): Employed to hold temporarily the right-hand
instruction from a word in memory.
• Program counter (PC): Contains the address of the next instruction pair to be
fetched from memory.
• Accumulator (AC) and multiplier quotient (MQ): Employed to hold temporarily
operands and results of ALU operations. For example, the result of
multiplying two 40-bit numbers is an 80-bit number; the most significant 40 bits
are stored in the AC and the least significant in the MQ.

## Slide 7: Embedded Systems
The use of electronics and software within a product
Billions of computer systems are produced each year that are embedded within larger devices
Today many devices that use electric power have an embedded computing system
Often embedded systems are tightly coupled to their environment
  This can give rise to real-time constraints imposed by the need to interact with the environment
    Constraints such as required speeds of motion, required precision of measurement, and required time durations, dictate the timing of software operations
  If multiple activities must be managed simultaneously this imposes more complex real-time constraints
Notes: The term embedded system refers to the use of electronics and software within a
product, as opposed to a general-purpose computer, such as a laptop or desktop
system. Millions of computers are sold every year, including laptops, personal
computers, workstations, servers, mainframes, and supercomputers. In contrast, billions
of computer systems are produced each year that are embedded within larger
devices. Today, many, perhaps most, devices that use electric power have an embedded
computing system. It is likely that in the near future virtually all such devices
will have embedded computing systems.
Types of devices with embedded systems are almost too numerous to list.
Examples include cell phones, digital cameras, video cameras, calculators, microwave
ovens, home security systems, washing machines, lighting systems, thermostats,
printers, various automotive systems (e.g., transmission control, cruise
control, fuel injection, anti-lock brakes, and suspension systems), tennis rackets,
toothbrushes, and numerous types of sensors and actuators in automated systems.
Often, embedded systems are tightly coupled to their environment. This can
give rise to real-time constraints imposed by the need to interact with the environment.
Constraints, such as required speeds of motion, required precision of measurement,
and required time durations, dictate the timing of software operations. If
multiple activities must be managed simultaneously, this imposes more complex
real-time constraints.

## Slide 8
Notes: Figure 1.14 shows in general terms an embedded system organization. In addition
to the processor and memory, there are a number of elements that differ from
the typical desktop or laptop computer:
■ There may be a variety of interfaces that enable the system to measure, manipulate,
and otherwise interact with the external environment. Embedded systems
often interact (sense, manipulate, and communicate) with external world
through sensors and actuators and hence are typically reactive systems; a reactive
system is in continual interaction with the environment and executes at a
pace determined by that environment.
■ The human interface may be as simple as a flashing light or as complicated as
real-time robotic vision. In many cases, there is no human interface.
■ The diagnostic port may be used for diagnosing the system that is being
controlled—not just for diagnosing the computer.
■ Special-purpose field programmable (FPGA), application-specific
(ASIC), or even nondigital hardware may be used to increase performance or reliability.
■ Software often has a fixed function and is specific to the application.
■ Efficiency is of paramount importance for embedded systems. They are optimized
for energy, code size, execution time, weight and dimensions, and cost.
There are several noteworthy areas of similarity to general-
purpose computer systems as well:
■ Even with nominally fixed function software, the ability to field upgrade to fix
bugs, to improve security, and to add functionality, has become very important
for embedded system, and not just in consumer devices.
■ One comparatively recent development has been of embedded system platforms
that support a wide variety of apps. Good examples of this are smartphones
and audio/visual devices, such as smart TVs.

## Slide 9: The Internet of Things (IoT)
Term that refers to the expanding interconnection of smart devices, ranging from appliances to tiny sensors
Is primarily driven by deeply embedded devices
Notes: It is worthwhile calling out separately one of the major drivers in the proliferation
of embedded systems. The Internet of things (IoT) is a term that refers to the
expanding interconnection of smart devices, ranging from appliances to tiny sensors.
A dominant theme is the embedding of short- range mobile transceivers into a wide
array of gadgets and everyday items, enabling new forms of communication between
people and things, and between things themselves. The Internet now supports the
interconnection of billions of industrial and personal objects, usually through cloud
systems. The objects deliver sensor information, act on their environment, and, in
some cases, modify themselves, to create overall management of a larger system, like
a factory or city.
The IoT is primarily driven by deeply embedded devices (defined below).
These devices are low-bandwidth, low-repetition data-capture, and low-bandwidth
data-usage appliances that communicate with each other and provide data via user
interfaces. Embedded appliances, such as high-resolution
video security cameras, video VoIP phones, and a handful of others, require high-bandwidth
streaming capabilities. Yet countless products simply require packets of data to be intermittently
delivered.
With reference to the end systems supported, the Internet has gone through
roughly four generations of deployment culminating in the IoT:
1. Information technology (IT) : PCs, servers, routers, firewalls, and so on, bought
as IT devices by enterprise IT people and primarily using wired connectivity
2. Operational technology (OT) : Machines/appliances with embedded IT built
by non-IT companies, such as medical machinery, SCADA (supervisory control
and data acquisition), process control, and kiosks, bought as appliances by
enterprise OT people and primarily using wired connectivity
3. Personal technology: Smartphones, tablets, and eBook readers bought as IT
devices by consumers (employees) exclusively using wireless connectivity and
often multiple forms of wireless connectivity
4. Sensor/actuator technology: Single-purpose devices bought by consumers, IT,
and OT people exclusively using wireless connectivity, generally of a single
form, as part of larger systems
It is the fourth generation that is usually thought of as the IoT, and it is marked
by the use of billions of embedded devices.

## Slide 10
There are two general approaches to developing an embedded operating system (OS):
  Take an existing OS and adapt it for the embedded application
  Design and implement an OS intended solely for embedded use
Application processors
  Defined by the processor’s ability to execute complex operating systems
  General-purpose in nature
  An example is the smartphone – the embedded system is designed to support numerous apps and perform a wide variety of functions
Dedicated processor
  Is dedicated to one or a small number of specific tasks required by the host device
  Because such an embedded system is dedicated to a specific task or tasks, the processor and associated components can be engineered to reduce size and cost
Embedded
Operating
Systems
Application Processors
versus
Dedicated Processors
Notes: There are two general approaches to developing an embedded operating system
(OS). The first approach is to take an existing OS and adapt it for the embedded
application. For example, there are embedded versions of Linux, Windows, and
Mac, as well as other commercial and proprietary operating systems specialized for
embedded systems. The other approach is to design and implement an OS intended
solely for embedded use. An example of the latter is TinyOS, widely used in wireless
sensor networks. This topic is explored in depth in [STAL15].
In this subsection, and the next two, we briefly introduce some terms commonly
found in the literature on embedded systems. Application processors are defined
by the processor’s ability to execute complex operating systems, such as Linux,
Android, and Chrome. Thus, the application processor is general-purpose in nature.
A good example of the use of an embedded application processor is the smartphone.
The embedded system is designed to support numerous apps and perform a wide
variety of functions.
Most embedded systems employ a dedicated processor , which, as the name
implies, is dedicated to one or a small number of specific tasks required by the host
device. Because such an embedded system is dedicated to a specific task or tasks,
the processor and associated components can be engineered to reduce size and cost.

## Slide 11
Notes: As we have seen, early microprocessor chips included registers, an ALU, and some
sort of control unit or instruction processing logic. As transistor density increased, it
became possible to increase the complexity of the instruction set architecture, and
ultimately to add memory and more than one processor. Contemporary microprocessor
chips, as shown in Figure 1.2, include multiple cores and a substantial amount
of cache memory.
A microcontroller chip makes a substantially different use of the logic space
available. Figure 1.15 shows in general terms the elements typically found on a microcontroller
chip. As shown, a microcontroller is a single chip that contains the processor,
non-volatile memory for the program (ROM), volatile memory for input and output
(RAM), a clock, and an I/O control unit. The processor portion of the microcontroller
has a much lower silicon area than other microprocessors and much higher energy efficiency.
We examine microcontroller organization in more detail in Section 1.6.
Also called a “computer on a chip,” billions of microcontroller units are
embedded each year in myriad products from toys to appliances to automobiles. For
example, a single vehicle can use 70 or more microcontrollers. Typically, especially
for the smaller, less expensive microcontrollers, they are used as dedicated processors
for specific tasks. For example, microcontrollers are heavily utilized in automation
processes. By providing simple reactions to input, they can control machinery,
turn fans on and off, open and close valves, and so forth. They are integral parts of
modern industrial technology and are among the most inexpensive ways to produce
machinery that can handle extremely complex functionalities.
Microcontrollers come in a range of physical sizes and processing power. Processors
range from 4-bit to 32-bit architectures. Microcontrollers tend to be much
slower than microprocessors, typically operating in the MHz range rather than the
GHz speeds of microprocessors. Another typical feature of a microcontroller is that
it does not provide for human interaction. The microcontroller is programmed for a
specific task, embedded in its device, and executes as and when required.

## Slide 12: Deeply Embedded Systems
Subset of embedded systems
Has a processor whose behavior is difficult to observe both by the programmer and the user
Uses a microcontroller rather than a microprocessor
Is not programmable once the program logic for the device has been burned into ROM
Has no interaction with a user
Dedicated, single-purpose devices that detect something in the environment, perform a basic level of processing, and then do something with the results
Often have wireless capability and appear in networked configurations, such as networks of sensors deployed over a large area
Typically have extreme resource constraints in terms of memory, processor size, time, and power consumption
Notes: We have, in this section, defined the concept of an embedded system. A subset of
embedded systems, and a quite numerous subset, is referred to as deeply embedded
systems . Although this term is widely used in the technical and commercial
literature, you will search the Internet in vain (or at least I did) for a straightforward
definition. Generally, we can say that a deeply embedded system has a processor
whose behavior is difficult to observe both by the programmer and the user.
A deeply embedded system uses a microcontroller rather than a microprocessor, is
not programmable once the program logic for the device has been burned into ROM
(read-only memory), and has no interaction with a user.
Deeply embedded systems are dedicated, single-purpose devices that detect something in the environment,
perform a basic level of processing, and then do
something with the results. Deeply embedded systems often have wireless capability
and appear in networked configurations, such as networks of sensors deployed
over a large area (e.g., factory, agricultural field). The Internet of things depends
heavily on deeply embedded systems. Typically, deeply embedded systems have
extreme resource constraints in terms of memory, processor size, time, and power
consumption.

## Slide 13: ARM
Refers to a processor architecture that has evolved from RISC design principles and is used in embedded systems
Family of RISC-based microprocessors and microcontrollers designed by ARM Holdings, Cambridge, England
Chips are high-speed processors that are known for their small die size and low power requirements
Probably the most widely used embedded processor architecture and indeed the most widely used processor architecture of any kind in the world
Acorn RISC Machine/Advanced RISC Machine
Notes: The ARM architecture refers to a processor architecture that has evolved from
RISC design principles and is used in embedded systems. Chapter 15 examines
RISC design principles in detail. In this section, we give a brief overview of the
ARM architecture.
ARM is a family of RISC-based
microprocessors and microcontrollers designed
by ARM Holdings, Cambridge, England. The company doesn’t make processors
but instead designs microprocessor and multicore architectures and licenses them
to manufacturers. Specifically, ARM Holdings has two types of licensable products:
processors and processor architectures. For processors, the customer buys the
rights to use ARM-supplied design in their own chips. For a processor architecture,
the customer buys the rights to design their own processor compliant with ARM’s
architecture.
ARM chips are high-speed
processors that are known for their small die size
and low power requirements. They are widely used in smartphones and other handheld
devices, including game systems, as well as a large variety of consumer products.
ARM chips are the processors in Apple’s popular iPod and iPhone devices,
and are used in virtually all Android smartphones as well. ARM is probably the
most widely used embedded processor architecture and indeed the most widely
used processor architecture of any kind in the world [VANC14].
The origins of ARM technology can be traced back to the British-based
Acorn Computers company. In the early 1980s, Acorn was awarded a contract by the British
Broadcasting Corporation (BBC) to develop a new microcomputer architecture
for the BBC Computer Literacy Project. The success of this contract enabled Acorn
to go on to develop the first commercial RISC processor, the Acorn RISC Machine
(ARM). The first version, ARM1, became operational in 1985 and was used for
internal research and development as well as being used as a coprocessor in the
BBC machine.
In this early stage, Acorn used the company VLSI Technology to do the actual
fabrication of the processor chips. VLSI was licensed to market the chip on its own
and had some success in getting other companies to use the ARM in their products,
particularly as an embedded processor.
The ARM design matched a growing commercial need for a high-performance,
Low-power-consumption, small-size, and low-cost
processor for embedded applications.
But further development was beyond the scope of Acorn’s capabilities.
Accordingly, a new company was organized, with Acorn, VLSI, and Apple Computer
as founding partners, known as ARM Ltd. The Acorn RISC Machine became
Advanced RISC Machines.

## Slide 14: ARM Products
Cortex-A/Cortex-A50
Cortex-R
Cortex-M
Cortex-M0
Cortex-M0+
Cortex-M3
Cortex-M4
Notes: ARM Holdings licenses a number of specialized microprocessors and related technologies,
but the bulk of their product line is the Cortex family of microprocessor
architectures. There are three Cortex architectures, conveniently labeled with the
initials A, R, and M.
The Cortex-Aand Cortex-A50
are application processors, intended for mobile devices such as smartphones and eBook readers,
as well as consumer devices such as digital TV and home gateways (e.g., DSL and
cable Internet modems). These processors run at higher clock frequency (over
1 GHz), and support a memory management unit (MMU), which is required for full
feature OSs such as Linux, Android, MS Windows, and mobile OSs. An MMU is
a hardware module that supports virtual memory and paging by translating virtual
addresses into physical addresses; this topic is explored in Chapter 8.
The two architectures use both the ARM and Thumb-2
instruction sets; the principal difference is that the Cortex-A
is a 32-bit machine, and the Cortex-A50 is a 64-bit machine.
The Cortex-R is designed to support real-time applications, in which the
timing of events needs to be controlled with rapid response to events. They can run at
a fairly high clock frequency (e.g., 200MHz to 800MHz) and have very low response
latency. The Cortex-R includes enhancements both to the instruction set and to the
processor organization to support deeply embedded real-time
devices. Most of these
processors do not have MMU; the limited data requirements and the limited number
of simultaneous processes eliminates the need for elaborate hardware and software
support for virtual memory. The Cortex-R
does have a Memory Protection Unit
(MPU), cache, and other memory features designed for industrial applications. An
MPU is a hardware module that prohibits one program in memory from accidentally
accessing memory assigned to another active program. Using various methods, a
protective boundary is created around the program, and instructions within the
program are prohibited from referencing data outside of that boundary.
Examples of embedded systems that would use the Cortex-R
are automotive braking systems, mass storage controllers, and networking and printing devices.
Cortex-M series processors have been developed primarily for the
microcontroller domain where the need for fast, highly deterministic interrupt
management is coupled with the desire for extremely low gate count and
lowest possible power consumption. As with the Cortex-R
series, the Cortex-M architecture has an MPU but no MMU. The Cortex-M
uses only the Thumb-2 instruction set. The market for the Cortex-M
includes IoT devices, wireless sensor/actuator networks used in factories and other enterprises, automotive
body electronics, and so on.
There are currently four versions of the Cortex-M
series:
■ Cortex-M0 :
Designed for 8- and 16-bit applications, this model emphasizes low
cost, ultra low power, and simplicity. It is optimized for small silicon die size
(starting from 12k gates) and use in the lowest cost chips.
■ Cortex-M0+ :
An enhanced version of the M0 that is more energy efficient.
■ Cortex-M3 :
Designed for 16- and 32-bit applications, this model emphasizes
performance and energy efficiency. It also has comprehensive debug and trace
features to enable software developers to develop their applications quickly.
■ Cortex-M4 :
This model provides all the features of the Cortex-M3,
with additional instructions to support digital signal processing tasks.
In this text, we will primarily use the ARM Cortex-M3
as our example embedded
system processor. It is the best suited of all ARM models for general-purpose
microcontroller use. The Cortex-M3 is used by a variety of manufacturers of microcontroller
products. Initial microcontroller devices from lead partners already
combine the Cortex-M3
processor with flash, SRAM, and multiple peripherals to
provide a competitive offering at the price of just $1.

## Slide 15: Cloud Computing
NIST defines cloud computing as:
“A model for enabling ubiquitous, convenient, on-demand network access to a shared pool of configurable computing resources that can be rapidly provisioned and released with minimal management effort or service provider interaction.”
You get economies of scale, professional network management, and professional security management
The individual or company only needs to pay for the storage capacity and services they need
Cloud provider takes care of security
Notes: Although the general concepts for cloud computing go back to the 1950s, cloud computing
services first became available in the early 2000s, particular targeted at large
enterprises. Since then, cloud computing has spread to small and medium size businesses,
and most recently to consumers. Apple’s iCloud was launched in 2012 and
had 20 million users within a week of launch. Evernote, the cloud-based notetaking
and archiving service, launched in 2008, approached 100 million users in less than
6 years. In this section, we provide a brief overview. Cloud computing is examined in
more detail in Chapter 17.
There is an increasingly prominent trend in many organizations to move a substantial
portion or even all information technology (IT) operations to an Internet-
connected infrastructure known as enterprise cloud computing. At the same time, individual
users of PCs and mobile devices are relying more and more on cloud computing
services to backup data, synch devices, and share, using personal cloud computing.
NIST defines cloud computing, in NIST SP-800-145 (The NIST Definition of Cloud
Computing ), as follows:
Cloud computing: A model for enabling ubiquitous, convenient, on-demand
network access to a shared pool of configurable computing resources (e.g., networks, servers,
storage, applications, and services) that can be rapidly provisioned and released with
minimal management effort or service provider interaction.
Basically, with cloud computing, you get economies of scale, professional network
management, and professional security management. These features can be
attractive to companies large and small, government agencies, and individual PC
and mobile users. The individual or company only needs to pay for the storage capacity
and services they need. The user, be it company or individual, doesn’t have
the hassle of setting up a database system, acquiring the hardware they need, doing
maintenance, and backing up the data—all these are part of the cloud service.
In theory, another big advantage of using cloud computing to store your data
and share it with others is that the cloud provider takes care of security. Alas, the
customer is not always protected. There have been a number of security failures
among cloud providers. Evernote made headlines in early 2013 when it told all of its
users to reset their passwords after an intrusion was discovered.

## Slide 16: Summary
Organization and architecture
Structure and function
Brief history of computers
  The First Generation: Vacuum tubes
  The Second Generation: Transistors
  The Third Generation: Integrated Circuits
  Later generations
  The evolution of the Intel x86 architecture
  Cloud computing
  Basic concepts
  Cloud services
Embedded systems
  The Internet of things
  Embedded operating systems
  Application processors versus dedicated processors
  Microprocessors versus microcontrollers
  Embedded versus deeply embedded systems
ARM architecture
  ARM evolution
  Instruction set architecture
  ARM products
Chapter 1
Basic Concepts and Computer Evolution
Notes: Chapter 1 summary.

## Slide 17: Chapter 2
Performance Issues
Notes: This chapter addresses the issue of computer system performance. We begin with a
consideration of the need for balanced utilization of computer resources, which provides
a perspective that is useful throughout the book. Next we look at contemporary
computer organization designs intended to provide performance to meet current
and projected demand. Finally, we look at tools and models that have been developed
to provide a means of assessing comparative computer system performance.

## Slide 18: Designing for Performance
The cost of computer systems continues to drop dramatically, while the performance and capacity of those systems continue to rise equally dramatically
Today’s laptops have the computing power of an IBM mainframe from 10 or 15 years ago
Processors are so inexpensive that we now have microprocessors we throw away
Desktop applications that require the great power of today’s microprocessor-based systems include:
  Image processing
  Three-dimensional rendering
  Speech recognition
  Videoconferencing
  Multimedia authoring
  Voice and video annotation of files
  Simulation modeling
  Businesses are relying on increasingly powerful servers to handle transaction and database processing and to support massive client/server networks that have replaced the huge mainframe computer centers of yesteryear
  Cloud service providers use massive high-performance banks of servers to satisfy high-volume, high-transaction-rate applications for a broad spectrum of clients
Notes: Year by year, the cost of computer systems continues to drop dramatically, while the
performance and capacity of those systems continue to rise equally dramatically.
Today’s laptops have the computing power of an IBM mainframe from 10 or 15
years ago. Thus, we have virtually “free” computer power. Processors are so inexpensive
that we now have microprocessors we throw away. The digital pregnancy test is
an example (used once and then thrown away). And this continuing technological
revolution has enabled the development of applications of astounding complexity
and power. For example, desktop applications that require the great power of
today’s microprocessor-based systems include
■ Image processing
■ Three-dimensional rendering
■ Speech recognition
■ Videoconferencing
■ Multimedia authoring
■ Voice and video annotation of files
■ Simulation modeling
Workstation systems now support highly sophisticated engineering and scientific
applications and have the capacity to support image and video applications. In addition,
businesses are relying on increasingly powerful servers to handle transaction
and database processing and to support massive client/server networks that have
replaced the huge mainframe computer centers of yesteryear. As well, cloud service
providers use massive high-performance banks of servers to satisfy high-volume,
high-transaction-rate applications for a broad spectrum of clients.
What is fascinating about all this from the perspective of computer organization
and architecture is that, on the one hand, the basic building blocks for today’s
computer miracles are virtually the same as those of the IAS computer from over
50 years ago, while on the other hand, the techniques for squeezing the maximum
performance out of the materials at hand have become increasingly sophisticated.
This observation serves as a guiding principle for the presentation in this
book. As we progress through the various elements and components of a computer,
two objectives are pursued. First, the book explains the fundamental functionality
in each area under consideration, and second, the book explores those techniques
required to achieve maximum performance. In the remainder of this section, we
highlight some of the driving factors behind the need to design for performance.

## Slide 19: Microprocessor Speed
Pipelining
Processor moves data or instructions into a conceptual pipe with all stages of the pipe processing simultaneously
Branch prediction
Processor looks ahead in the instruction code fetched from memory and predicts which branches, or groups of instructions, are likely to be processed next
Data flow analysis
Processor analyzes which instructions are dependent on each other’s results, or data, to create an optimized schedule of instructions
Speculative execution
Using branch prediction and data flow analysis, some processors speculatively execute instructions ahead of their actual appearance in the program execution, holding the results in temporary locations, keeping execution engines as busy as possible
Superscalar execution
This is the ability to issue more than one instruction in every processor clock cycle. (In effect, multiple parallel pipelines are used.)
Techniques built into contemporary processors include:
Notes: What gives Intel x86 processors or IBM mainframe computers such mind-boggling
power is the relentless pursuit of speed by processor chip manufacturers. The evolution
of these machines continues to bear out Moore’s law, mentioned previously. So
long as this law holds, chipmakers can unleash a new generation of chips every three
years—with four times as many transistors. In memory chips, this has quadrupled
the capacity of dynamic random-access memory (DRAM), still the basic technology
for computer main memory, every three years. In microprocessors, the addition of
new circuits, and the speed boost that comes from reducing the distances between
them, has improved performance four- or fivefold every three years or so since Intel
launched its x86 family in 1978.
But the raw speed of the microprocessor will not achieve its potential unless
it is fed a constant stream of work to do in the form of computer instructions.
Anything that gets in the way of that smooth flow undermines the power of the
processor. Accordingly, while the chipmakers have been busy learning how to fabricate
chips of greater and greater density, the processor designers must come up with
ever more elaborate techniques for feeding the monster. Among the techniques
built into contemporary processors are the following:
Pipelining:
The execution of an instruction involves multiple stages of operation,
including fetching the instruction, decoding the opcode, fetching operands,
performing a calculation, and so on. Pipelining enables a processor to
work simultaneously on multiple instructions by performing a different phase
for each of the multiple instructions at the same time. The processor overlaps
operations by moving data or instructions into a conceptual pipe with all
stages of the pipe processing simultaneously. For example, while one instruction
is being executed, the computer is decoding the next instruction. This is
the same principle as seen in an assembly line.
• Branch prediction:
The processor looks ahead in the instruction code fetched
from memory and predicts which branches, or groups of instructions, are likely
to be processed next. If the processor guesses right most of the time, it can
prefetch the correct instructions and buffer them so that the processor is kept
busy. The more sophisticated examples of this strategy predict not just the
next branch but multiple branches ahead. Thus, branch prediction increases
the amount of work available for the processor to execute.
• Superscalar execution:
This is the ability to issue more than one instruction
in every processor clock cycle. In effect, multiple parallel pipelines are used.
• Data flow analysis:
The processor analyzes which instructions are dependent
on each other’s results, or data, to create an optimized schedule of instructions.
In fact, instructions are scheduled to be executed when ready, independent of
the original program order. This prevents unnecessary delay.
• Speculative execution:
Using branch prediction and data flow analysis, some
processors speculatively execute instructions ahead of their actual appearance
in the program execution, holding the results in temporary locations.
This enables the processor to keep its execution engines as busy as possible by
executing instructions that are likely to be needed.
These and other sophisticated techniques are made necessary by the sheer
power of the processor. Collectively they make it possible to execute many instructions
per processor cycle, rather than to take many cycles per instruction.

## Slide 20: Performance Balance
Increase the number of bits that are retrieved at one time by making DRAMs “wider” rather than “deeper” and by using wide bus data paths
Change the DRAM interface to make it more efficient by including a cache or other buffering scheme on the DRAM chip
Reduce the frequency of memory access by incorporating increasingly complex and efficient cache structures between the processor and main memory
Increase the interconnect bandwidth between processors and memory by using higher speed buses and a hierarchy of buses to buffer and structure data flow
  Adjust the organization and
  architecture to compensate
  for the mismatch among the
  capabilities of the various
  components
  Architectural examples
  include:
Notes: While processor power has raced ahead at breakneck speed, other critical components
of the computer have not kept up. The result is a need to look for performance
balance: an adjusting of the organization and architecture to compensate for the
mismatch among the capabilities of the various components.
The problem created by such mismatches is particularly critical at the
interface between processor and main memory. While processor speed has grown
rapidly, the speed with which data can be transferred between main memory and the
processor has lagged badly. The interface between processor and main memory is
the most crucial pathway in the entire computer because it is responsible for carrying
a constant flow of program instructions and data between memory chips and the
processor. If memory or the pathway fails to keep pace with the processor’s insistent
demands, the processor stalls in a wait state, and valuable processing time is lost.
A system architect can attack this problem in a number of ways, all of which
are reflected in contemporary computer designs. Consider the following examples:
• Increase the number of bits that are retrieved at one time by making DRAMs
“wider” rather than “deeper” and by using wide bus data paths.
• Change the DRAM interface to make it more efficient by including a cache
or other buffering scheme on the DRAM chip.
• Reduce the frequency of memory access by incorporating increasingly complex
and efficient cache structures between the processor and main memory. This
includes the incorporation of one or more caches on the processor chip as well
as on an off-chip cache close to the processor chip.
• Increase the interconnect bandwidth between processors and memory by using
higher-speed buses and a hierarchy of buses to buffer and structure data
flow.

## Slide 21
Notes: Another area of design focus is the handling of I/O devices. As computers
become faster and more capable, more sophisticated applications are developed
that support the use of peripherals with intensive I/O demands. Figure 2.1 gives
some examples of typical peripheral devices in use on personal computers and
workstations. These devices create tremendous data throughput demands. While
the current generation of processors can handle the data pumped out by these
devices, there remains the problem of getting that data moved between processor
and peripheral. Strategies here include caching and buffering schemes plus the
use of higher-speed interconnection buses and more elaborate structures of buses.
In addition, the use of multiple-processor configurations can aid in satisfying I/O
demands.
The key in all this is balance. Designers constantly strive to balance the
throughput and processing demands of the processor components, main memory,
I/O devices, and the interconnection structures. This design must constantly be
rethought to cope with two constantly evolving factors:
• The rate at which performance is changing in the various technology areas
(processor, buses, memory, peripherals) differs greatly from one type of
element to another.
• New applications and new peripheral devices constantly change the nature of
the demand on the system in terms of typical instruction profile and the data
access patterns.
Thus, computer design is a constantly evolving art form. This book attempts to
present the fundamentals on which this art form is based and to present a survey of
the current state of that art.

## Slide 22: Improvements in Chip Organization and Architecture
Increase hardware speed of processor
  Fundamentally due to shrinking logic gate size
    More gates, packed more tightly, increasing clock rate
    Propagation time for signals reduced
Increase size and speed of caches
  Dedicating part of processor chip
    Cache access times drop significantly
Change processor organization and architecture
  Increase effective speed of instruction execution
  Parallelism
Notes: As designers wrestle with the challenge of balancing processor performance with that
of main memory and other computer components, the need to increase processor
speed remains. There are three approaches to achieving increased processor speed:
• Increase the hardware speed of the processor. This increase is fundamentally
due to shrinking the size of the logic gates on the processor chip, so that more
gates can be packed together more tightly and to increasing the clock rate.
With gates closer together, the propagation time for signals is significantly
reduced, enabling a speeding up of the processor. An increase in clock rate
means that individual operations are executed more rapidly.
• Increase the size and speed of caches that are interposed between the processor
and main memory. In particular, by dedicating a portion of the processor
chip itself to the cache, cache access times drop significantly.
• Make changes to the processor organization and architecture that increase the
effective speed of instruction execution. Typically, this involves using parallelism
in one form or another.

## Slide 23: Multicore
The use of multiple processors on the same chip provides the potential to increase performance without increasing the clock rate
Strategy is to use two simpler processors on the chip rather than one more complex processor
With two processors larger caches are justified
As caches became larger it made performance sense to create two and then three levels of cache on a chip
Notes: With all of the difficulties cited in the preceding paragraphs in mind, designers
have turned to a fundamentally new approach to improving performance: placing
multiple processors on the same chip, with a large shared cache. The use of multiple
processors on the same chip, also referred to as multiple cores, or multicore,
provides the potential to increase performance without increasing the clock rate.
Studies indicate that, within a processor, the increase in performance is roughly
proportional to the square root of the increase in complexity [BORK03]. But if the
software can support the effective use of multiple processors, then doubling the
number of processors almost doubles performance. Thus, the strategy is to use two
simpler processors on the chip rather than one more complex processor.
In addition, with two processors, larger caches are justified. This is important
because the power consumption of memory logic on a chip is much less than that of
processing logic.
As the logic density on chips continues to rise, the trend to both more cores
and more cache on a single chip continues. Two-core chips were quickly followed
by four-core chips, then 8, then 16, and so on. As the caches became larger, it made
performance sense to create two and then three levels of cache on a chip, with the
first-level cache dedicated to an individual processor and levels two and three being
shared by all the processors. It is now common for the second-level
cache to also be private to each core.

## Slide 24: Many Integrated Core (MIC) Graphics Processing Unit (GPU)
Leap in performance as well as the challenges in developing software to exploit such a large number of cores
The multicore and MIC strategy involves a homogeneous collection of general purpose processors on a single chip
Core designed to perform parallel operations on graphics data
Traditionally found on a plug-in graphics card, it is used to encode and render 2D and 3D graphics as well as process video
Used as vector processors for a variety of applications that require repetitive computations
MIC
GPU
Notes: Chip manufacturers are now in the process of making a huge leap forward
in the number of cores per chip, with more than 50 cores per chip. The leap in
performance as well as the challenges in developing software to exploit such a large
number of cores have led to the introduction of a new term: many integrated core
(MIC).
The multicore and MIC strategy involves a homogeneous collection of
general-purpose processors on a single chip. At the same time, chip manufacturers
are pursuing another design option: a chip with multiple general-purpose processors
plus graphics processing units (GPUs) and specialized cores for video processing
and other tasks. In broad terms, a GPU is a core designed to perform parallel
operations on graphics data. Traditionally found on a plug-in graphics card (display
adapter), it is used to encode and render 2D and 3D graphics as well as process
video.
Since GPUs perform parallel operations on multiple sets of data, they are
increasingly being used as vector processors for a variety of applications that
require repetitive computations. This blurs the line between the GPU and the
CPU [FATA08, PROP11]. When a broad range of applications are supported
by such a processor, the term general-purpose computing on GPUs (GPGPU)
is used.
We explore design characteristics of multicore computers in Chapter 18 and
GPGPUs in Chapter 19.

## Slide 25: Amdahl’s Law
Gene Amdahl
Deals with the potential speedup of a program using multiple processors compared to a single processor
Illustrates the problems facing industry in the development of multi-core machines
  Software must be adapted to a highly parallel execution environment to exploit the power of parallel processing
Can be generalized to evaluate and design technical improvement in a computer system
Notes: Computer system designers look for ways to improve system performance by
advances in technology or change in design. Examples include the use of parallel
processors, the use of a memory cache hierarchy, and speedup in memory access
time and I/O transfer rate due to technology improvements. In all of these cases, it is
important to note that a speedup in one aspect of the technology or design does not
result in a corresponding improvement in performance. This limitation is succinctly
expressed by Amdahl’s law.
Amdahl’s law was first proposed by Gene Amdahl in 1967 ([AMDA67],
[AMDA13]) and deals with the potential speedup of a program using multiple processors
compared to a single processor.
Nevertheless, Amdahl’s law illustrates the problems facing industry in the development
of multicore machines with an ever-growing number of cores: The software
that runs on such machines must be adapted to a highly parallel execution environment
to exploit the power of parallel processing.
Amdahl’s law can be generalized to evaluate any design or technical improvement
in a computer system.

## Slide 26
Speedup = Original/Advanced
O=T
A= (1-f)T + fT/N
Speedup= T/((1-f)T + fT/N)
=1/ ((1-f) + f/N)
10Pocessors, f=0.5 ????
Notes: Consider a program running on a single processor such that a fraction
(1 – f) of the execution time involves code that is inherently serial and a fraction
f that involves code that is infinitely parallelizable with no scheduling overhead.
Let T be the total execution time of the program using a single processor. Then the
speedup using a parallel processor with N processors that fully exploits the parallel
portion of the program is as follows:
Speedup =
Time to execute program on a single processor
Time to execute program on N parallel processors
=T(1 - f) + Tf
T(1 - f) +Tf
N
= 1
(1 - f) +f
N
This equation is illustrated in Figures 2.3 and 2.4.

## Slide 27
S=1/ ((1-f) + f/N)
Notes: Two important conclusions can be
drawn:
1. When f is small, the use of parallel processors has little effect.
2. As N approaches infinity, speedup is bound by 1/(1 – f), so that there are
diminishing returns for using more processors.
These conclusions are too pessimistic, an assertion first put forward in
[GUST88]. For example, a server can maintain multiple threads or multiple tasks
to handle multiple clients and execute the threads or tasks in parallel up to the limit
of the number of processors. Many database applications involve computations on
massive amounts of data that can be split up into multiple parallel tasks.

## Slide 28
clock cycle time(τ)=1/clock frequency(f)
Notes: Operations performed by a processor, such as fetching an
instruction, decoding the instruction, performing an arithmetic operation, and so
on, are governed by a system clock. Typically, all operations begin with the pulse of
the clock. Thus, at the most fundamental level, the speed of a processor is dictated
by the pulse frequency produced by the clock, measured in cycles per second, or
Hertz (Hz).
Typically, clock signals are generated by a quartz crystal, which generates a
constant sine wave while power is applied. This wave is converted into a digital
voltage pulse stream that is provided in a constant flow to the processor circuitry
(Figure 2.5). For example, a 1-GHz processor receives 1 billion pulses per second.
The rate of pulses is known as the clock rate, or clock speed. One increment, or
pulse, of the clock is referred to as a clock cycle, or a clock tick. The time between
pulses is the cycle time.
The clock rate is not arbitrary, but must be appropriate for the physical layout
of the processor. Actions in the processor require signals to be sent from one processor
element to another. When a signal is placed on a line inside the processor, it
takes some finite amount of time for the voltage levels to settle down so that an
accurate value (1 or 0) is available. Furthermore, depending on the physical layout
of the processor circuits, some signals may change more rapidly than others. Thus,
operations must be synchronized and paced so that the proper electrical signal
(voltage) values are available for each operation.
The execution of an instruction involves a number of discrete steps, such
as fetching the instruction from memory, decoding the various portions of the
instruction, loading and storing data, and performing arithmetic and logical operations.
Thus, most instructions on most processors require multiple clock cycles to
complete. Some instructions may take only a few cycles, while others require dozens.
In addition, when pipelining is used, multiple instructions are being executed simultaneously.
Thus, a straight comparison of clock speeds on different processors does
not tell the whole story about performance.

## Slide 29
Table 2.1 Performance Factors and System Attributes
T = Ic ∙ CPI ∙ τ
= Ic ∙ (p + m ∙ k) ∙ τ
Notes: Table 2.1 is a matrix in which one dimension shows the five
performance factors and the other dimension shows the four system attributes. An
X in a cell indicates a system attribute that affects a performance factor.
A common measure of performance for a processor is the rate at which
instructions are executed, expressed as millions of instructions per second (MIPS),
referred to as the MIPS rate.
Another common performance measure deals only with floating-point instructions.
These are common in many scientific and game applications. Floating-point
performance is expressed as millions of floating-point operations per second
(MFLOPS).

## Slide 30: Calculating the Mean
The use of benchmarks to compare systems involves calculating the mean value of a set of data points related to execution time
The three common formulas used for calculating a mean are:
Arithmetic
Geometric
Harmonic
Notes: In evaluating some aspect of computer system performance, it is often the case that a
single number, such as execution time or memory consumed, is used to characterize
performance and to compare systems. Clearly, a single number can provide only a
very simplified view of a system’s capability. Nevertheless, and especially in the field
of benchmarking, single numbers are typically used for performance comparison
[SMIT88].
As is discussed in Section 2.6, the use of benchmarks to compare systems
involves calculating the mean value of a set of data points related to execution
time. It turns out that there are multiple alternative algorithms that can be used
for calculating a mean value, and this has been the source of some controversy in
the benchmarking field. In this section, we define these alternative algorithms and
comment on some of their properties. This prepares us for a discussion in the next
section of mean calculation in benchmarking.
The three common formulas used for calculating a mean are arithmetic, geometric,
and harmonic.

## Slide 31
An Arithmetic Mean (AM) is an appropriate measure if the sum of all the measurements is a meaningful and interesting value
The AM is a good candidate for comparing the execution time performance of several systems
Arithmetic
Mean
For example, suppose we were interested in using a system
for large-scale simulation studies and wanted to evaluate several alternative products. On each system we could run the simulation multiple times with different input values for each run, and then take the average execution time across all runs. The use of
multiple runs with different inputs should ensure that the results are not heavily biased by some unusual feature of a given input set. The AM of all the runs is a good measure of the system’s performance on simulations, and a good number to use for system comparison.
The AM used for a time-based variable, such as program execution time, has the important property that it is directly proportional to the total time
  If the total time doubles, the mean value doubles
Notes: An AM is an appropriate measure if the sum of all the measurements is a meaningful
and interesting value. The AM is a good candidate for comparing the execution time performance
of several systems. For example, suppose we were interested in using a system
for large-scale simulation studies and wanted to evaluate several alternative products.
On each system we could run the simulation multiple times with different input values
for each run, and then take the average execution time across all runs. The use of
multiple runs with different inputs should ensure that the results are not heavily biased
by some unusual feature of a given input set. The AM of all the runs is a good measure of
the system’s performance on simulations, and a good number to use for system comparison.
The AM used for a time-based variable (e.g., seconds), such as program execution
time, has the important property that it is directly proportional to the total
time. So, if the total time doubles, the mean value doubles.

## Slide 32
60Km
4hrs, 15Km/h
2hrs, 30Km/h
Average time :
Average speed :
HM<GM<AM

## Slide 33
Table 2.2
A Comparison of Arithmetic and
Harmonic Means for Rates
M=106
108 floating point
operations.
Notes: A simple numerical example will illustrate the difference between the
two means in calculating a mean value of the rates, shown in Table 2.2. The table compares
the performance of three computers on the execution of two programs. For simplicity, we
assume that the execution of each program results in the execution of 108 floating-point
operations. The left half of the table shows the execution times for each computer running
each program, the total execution time, and the AM of the execution times. Computer
A executes in less total time than B, which executes in less total time than C, and this is
reflected accurately in the AM.
The right half of the table provides a comparison in terms of rates, expressed
in MFLOPS. The rate calculation is straightforward. For example, program 1 executes
100 million floating-point operations. Computer A takes 2 seconds to execute the program
for a MFLOPS rate of 100/2 = 50. Next, consider the AM of the rates. The greatest value
is for computer A, which suggests that A is the fastest computer. In terms of total execution
time, A has the minimum time, so it is the fastest computer of the three. But the AM
of rates shows B as slower than C, whereas in fact B is faster than C. Looking at the HM
values, we see that they correctly reflect the speed ordering of the computers. This confirms
that the HM is preferred when calculating rates.
The reader may wonder why go through all this effort. If we want to compare
execution times, we could simply compare the total execution times of the three
systems. If we want to compare rates, we could simply take the inverse of the total
execution time, as shown in the table. There are two reasons for doing the individual
calculations rather than only looking at the aggregate numbers:
1. A customer or researcher may be interested not only in the overall average
performance but also performance against different types of benchmark programs,
such as business applications, scientific modeling, multimedia applications,
and systems programs. Thus, a breakdown by type of benchmark is
needed as well as a total.
2. Usually, the different programs used for evaluation are weighted differently.
In Table 2.2, it is assumed that the two test programs execute the same number
of operations. If that is not the case, we may want to weight accordingly.
Or different programs could be weighted differently to reflect importance or
priority.

## Slide 34
Notes: A simple example will illustrate the way in which the GM exhibits consistency
for normalized results. In Table 2.3, we use the same performance results as were
used in Table 2.2. In Table 2.3a, all results are normalized to Computer A, and the means
are calculated on the normalized values. Based on total execution time, A is faster than
B, which is faster than C. Both the AMs and GMs of the normalized times reflect this. In
Table 2.3b, the systems are now normalized to B. Again the GMs correctly reflect the relative
speeds of the three computers, but now the AM produces a different ordering.

## Slide 35: Benchmark Principles
Desirable characteristics of a benchmark program:
  It is written in a high-level language, making it portable across different machines
  It is representative of a particular kind of programming domain or paradigm, such as systems programming, numerical programming, or commercial programming
  It can be measured easily
  It has wide distribution
Notes: Measures such as MIPS and MFLOPS have proven inadequate to evaluating the performance
of processors. Because of differences in instruction sets, the instruction execution
rate is not a valid means of comparing the performance of different architectures.
Another consideration is that the performance of a given processor on a given
program may not be useful in determining how that processor will perform on a
very different type of application. Accordingly, beginning in the late 1980s and
early 1990s, industry and academic interest shifted to measuring the performance of
systems using a set of benchmark programs. The same set of programs can be run on
different machines and the execution times compared. Benchmarks provide guidance
to customers trying to decide which system to buy and can be useful to vendors
and designers in determining how to design systems to meet benchmark goals.
[WEIC90] lists the following as desirable characteristics of a benchmark program:
1. It is written in a high-level language, making it portable across different machines.
2. It is representative of a particular kind of programming domain or paradigm, such
as systems programming, numerical programming, or commercial programming.
3. It can be measured easily.
4. It has wide distribution.

## Slide 36: System Performance Evaluation Corporation (SPEC)
Benchmark suite
  A collection of programs, defined in a high-level language
  Together attempt to provide a representative test of a computer in a particular application or system programming area
  SPEC
  An industry consortium
  Defines and maintains the best known collection of benchmark suites aimed at evaluating computer systems
  Performance measurements are widely used for comparison and research purposes
Notes: The common need in industry and academic and research
communities for generally accepted computer performance measurements has
led to the development of standardized benchmark suites. A benchmark suite is a
collection of programs, defined in a high-level language, that together attempt to
provide a representative test of a computer in a particular application or system
programming area. The best known such collection of benchmark suites is defined
and maintained by the System Performance Evaluation Corporation (SPEC),
an industry consortium. SPEC performance measurements are widely used for
comparison and research purposes.

## Slide 37: SPEC CPU2006
Best known SPEC benchmark suite
Industry standard suite for processor intensive applications
Appropriate for measuring performance for applications that spend most of their time doing computation rather than I/O
Consists of 17 floating point programs written in C, C++, and Fortran and 12 integer programs written in C and C++
Suite contains over 3 million lines of code
Fifth generation of processor intensive suites from SPEC
Notes: The best known of the SPEC benchmark suites is SPEC CPU2006. This is the
industry standard suite for processor-intensive applications. That is, SPEC CPU2006 is
appropriate for measuring performance for applications that spend most of their time
doing computation rather than I/O.
The CPU2006 suite is based on existing applications
that have already been ported to a wide variety of platforms by SPEC industry
members. It consists of 17 floating-point programs written in C, C++, and Fortran; and
12 integer programs written in C and C++. The suite contains over 3 million lines of
code. This is the fifth generation of processor-intensive suites from SPEC, replacing
SPEC CPU2000, SPEC CPU95, SPEC CPU92, and SPEC CPU89 [HENN07].
Other SPEC suites include the following:
• SPECjvm98: Intended to evaluate performance of the combined hardware
and software aspects of the Java Virtual Machine (JVM) client platform
• SPECjbb2000 (Java Business Benchmark): A benchmark for evaluating
server-side Java-based electronic commerce applications
• SPECweb99: Evaluates the performance of World Wide Web (WWW) servers
• SPECmail2001: Designed to measure a system’s performance acting as a mail
server

## Slide 38: Summary
Designing for performance
  Microprocessor speed
  Performance balance
  Improvements in chip organization and architecture
Multicore
MICs
GPGPUs
Amdahl’s Law
Little’s Law
  Basic measures of computer performance
  Clock speed
  Instruction execution rate
  Calculating the mean
  Arithmetic mean
  Harmonic mean
  Geometric mean
  Benchmark principles
  SPEC benchmarks
Chapter 2
Performance
Issues
Notes: Chapter 2 summary.