## Slide 1: William Stallings Computer Organization and Architecture 10th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 10/e, by William Stallings, Chapter 15 “Reduced Instruction Set Computers”.

## Slide 2: Pipelining Strategy
Similar to the use of an assembly line in a manufacturing plant
New inputs are accepted at one end before previously accepted inputs appear as outputs at the other end
To apply this concept to instruction execution we must recognize that an instruction has a number of stages
Notes: 38
Instruction pipelining is similar to the use of an assembly line in a manufacturing plant. An assembly line takes advantage of the fact that a product goes through various stages of production. By laying the production process out in an assembly line, products at various stages can be worked on simultaneously. This process is also referred to as pipelining, because, as in a pipeline, new inputs are accepted at one end before previously accepted inputs appear as outputs at the other end.
To apply this concept to instruction execution, we must recognize that, in fact, an instruction has a number of stages. Figures 14.5, for example, breaks the instruction cycle up into 10 tasks, which occur in sequence. Clearly, there should be some opportunity for pipelining.

## Slide 3
Notes: 39
For the sake of illustration, let us assume equal duration. Using this assumption, Figure 14.10 shows that a six-stage pipeline can reduce the execution time for 9 instructions from 54 time units to 14 time units.
Several comments are in order: The diagram assumes that each instruction goes through all six stages of the pipeline. This will not always be the case. For example, a load instruction does not need the WO stage. However, to simplify the pipeline hardware, the timing is set up assuming that each instruction requires all six stages. Also, the diagram assumes that all of the stages can be performed in parallel. In particular, it is assumed that there are no memory conflicts. For example, the FI, FO, and WO stages involve a memory access. The diagram implies that all these accesses can occur simultaneously. Most memory systems will not permit that. However, the desired value may be in cache, or the FO or WO stage may be null. Thus, much of the time, memory conflicts will not slow down the pipeline.

## Slide 4
Processing time without pipeline
T1 = n × k × t
Processing time without pipeline
T2 = k × t + (n-1) × t = (k + n -1) × t
Speedup = T1/T2
= (n × k × t) / {(k + n -1) × t }
= (n × k )/ (k + n -1)
When n goes towards ∞, speedup =
Notes: Figure 14.14a plots the speedup factor as a function of the number of instructions that are executed without a branch.
Figure 14.14b shows the speedup factor as a function of the number of stages in the instruction pipeline
Thus, the larger the number of pipeline stages, the greater the potential for speedup. However, as a practical matter, the potential gains of additional pipe- line stages are countered by increases in cost, delays between stages, and the fact that branches will be encountered requiring the flushing of the pipeline.

## Slide 5
Notes: 40
Several other factors serve to limit the performance enhancement. If the six stages are not of equal duration, there will be some waiting involved at various pipe- line stages, as discussed before for the two-stage pipeline. Another difficulty is the conditional branch instruction, which can invalidate several instruction fetches. A similar unpredictable event is an interrupt. Figure 14.11 illustrates the effects of the conditional branch, using the same program as Figure 14.10. Assume that instruction 3 is a conditional branch to instruction 15. Until the instruction is executed, there is no way of knowing which instruction will come next. The pipeline, in this example, simply loads the next instruction in sequence (instruction 4) and proceeds. In Figure 14.10, the branch is not taken, and we get the full performance benefit of the enhancement. In Figure 14.11, the branch is taken. This is not determined until the end of time unit 7. At this point, the pipeline must be cleared of instructions that are not useful. During time unit 8, instruction 15 enters the pipeline. No instructions complete during time units 9 through 12; this is the performance penalty incurred because we could not anticipate the branch.

## Slide 6: Pipeline Hazards
Occur when the pipeline, or some portion of the pipeline, must stall because conditions do not permit continued execution
Also referred to as a pipeline bubble
There are three types of hazards:
Resource
Data
Control
Notes: In the previous subsection, we mentioned some of the situations that can result in less than optimal pipeline performance. In this subsection, we examine this issue in a more systematic way. Chapter 16 revisits this issue, in more detail, after we have introduced the complexities found in superscalar pipeline organizations.
A pipeline hazard occurs when the pipeline, or some portion of the pipeline, must stall because conditions do not permit continued execution. Such a pipe- line stall is also referred to as a pipeline bubble. There are three types of hazards: resource, data, and control.

## Slide 7: Interrupt Processing
Interrupts
  Generated by a signal from hardware and it may occur at random times during the execution of a program
  Maskable
  Nonmaskable
Exceptions
  Generated from software and is provoked by the execution of an instruction
  Processor detected
  Programmed
Interrupt vector table
  Every type of interrupt is assigned a number
  Number is used to index into the interrupt vector table
Interrupts and Exceptions
Notes: Two classes of events cause the x86 to suspend execution of the current instruction stream and respond to the event: interrupts and exceptions. In both cases, the processor saves the context of the current process and transfers to a predefined routine to service the condition. An interrupt is generated by a signal from hardware, and it may occur at random times during the execution of a program. An exception is generated from software, and it is provoked by the execution of an instruction. There are two sources of interrupts and two sources of exceptions:
1. Interrupts
  Maskable interrupts: Received on the processor’s INTR pin. The processor does not recognize a maskable interrupt unless the interrupt enable flag (IF) is set.
  Nonmaskable interrupts: Received on the processor’s NMI pin. Recognition of such interrupts cannot be prevented.
  2. Exceptions
  Processor-detected exceptions: Results when the processor encounters an
  error while attempting to execute an instruction.
  Programmed exceptions: These are instructions that generate an exception (e.g., INTO, INT3, INT, and BOUND).
Interrupt processing on the x86 uses the interrupt vector table. Every type of interrupt is assigned a number, and this number is used to index into the interrupt vector table. This table contains 256 32-bit interrupt vectors, which is the address (segment and offset) of the interrupt service routine for that interrupt number.

## Slide 8: The ARM Processor
Moderate array of uniform registers
A load/store model of data processing in which operations only perform on operands in registers and not directly in memory
A uniform fixed-length instruction of 32 bits for the standard set and 16 bits for the Thumb instruction set
Separate arithmetic logic unit (ALU) and shifter units
A small number of addressing modes with all load/store addresses determined from registers and instruction fields
Auto-increment and auto-decrement addressing modes are used to improve the operation of program loops
Conditional execution of instructions minimizes the need for conditional branch instructions, thereby improving pipeline efficiency, because pipeline flushing is reduced
ARM is primarily a RISC system with the following attributes:
Notes: ARM is primarily a RISC system with the following notable attributes:
• A moderate array of uniform registers, more than are found on some CISC systems but fewer than are found on many RISC systems.
* A load/store model of data processing, in which operations only perform on operands in registers and not directly in memory. All data must be loaded into registers before an operation can be performed; the result can then be used for further processing or stored into memory.
* A uniform fixed-length instruction of 32 bits for the standard set and 16 bits for the Thumb instruction set.
* To make each data processing instruction more flexible, either a shift or rotation can preprocess one of the source registers. To efficiently support this feature, there are separate arithmetic logic unit (ALU) and shifter units.
A small number of addressing modes with all load/store addressees deter- mined from registers and instruction fields. Indirect or indexed addressing involving values in memory are not used.
Auto-increment and auto-decrement addressing modes are used to improve the operation of program loops.
Conditional execution of instructions minimizes the need for conditional branch instructions, thereby improving pipeline efficiency, because pipeline flushing is reduced.

## Slide 9: Chapter 15
Reduced Instruction Set Computers (RISC)
Notes: Since the development of the stored-program computer around 1950, there have been remarkably few true innovations in the areas of computer organization and architecture. The following are some of the major advances since the birth of the computer:
The family concept: Introduced by IBM with its System/360 in 1964, followed shortly thereafter by DEC, with its PDP-8. The family concept decouples the architecture of a machine from its implementation. A set of computers is offered, with different price/performance characteristics, that presents the same architecture to the user. The differences in price and performance are due to different implementations of the same architecture.
Microprogrammed control unit: Suggested by Wilkes in 1951 and introduced by IBM on the S/360 line in 1964. Microprogramming eases the task of designing and implementing the control unit and provides support for the family concept.
Cache memory: First introduced commercially on IBM S/360 Model 85 in 1968. The insertion of this element into the memory hierarchy dramatically improves performance.
Pipelining: A means of introducing parallelism into the essentially sequential nature of a machine-instruction program. Examples are instruction pipelining and vector processing.
Multiple processors: This category covers a number of different organizations and objectives.
Reduced instruction set computer (RISC) architecture: This is the focus of this chapter.
When it appeared, RISC architecture was a dramatic departure from the historical trend in processor architecture. An analysis of the RISC architecture brings into focus many of the important issues in computer organization and architecture.
Although RISC architectures have been defined and designed in a variety of
ways by different groups, the key elements shared by most designs are these:
A large number of general-purpose registers, and/or the use of compiler technology to optimize register usage
A limited and simple instruction set
An emphasis on optimizing the instruction pipeline
We begin this chapter with a brief survey of some results on instruction sets, and then examine each of the three topics just listed. This is followed by a description of two of the best-documented RISC designs.

## Slide 10: Supersca l ar
Term first coined in 1987
Refers to a machine that is designed to improve the performance of the execution of scalar instructions
In most applications the bulk of the operations are on scalar quantities
Represents the next step in the evolution of high-performance general-purpose processors
Essence of the approach is the ability to execute instructions independently and concurrently in different pipelines
Concept can be further exploited by allowing instructions to be executed in an order different from the program order
Overview
Notes: The term superscalar, first coined in 1987 [AGER87], refers to a machine that is designed to improve the performance of the execution of scalar instructions. In most applications, the bulk of the operations are on scalar quantities. Accordingly, the superscalar approach represents the next step in the evolution of high-performance general-purpose processors.
The essence of the superscalar approach is the ability to execute instructions independently and concurrently in different pipelines. The concept can be further exploited by allowing instructions to be executed in an order different from the program order.

## Slide 11
Notes: Figure 16.1 compares, in general terms, the scalar and superscalar approaches. In a traditional scalar organization, there is a single pipelined functional unit for integer operations and one for floating-point operations. Parallelism is achieved by enabling multiple instructions to be at different stages of the pipeline at one time. In the superscalar organization, there are multiple functional units, each of which is implemented as a pipeline. Each individual functional unit provides a degree of parallelism by virtue of its pipelined structure. The use of multiple functional units enables the processor to execute streams of instructions in parallel, one stream for each pipeline. It is the responsibility of the hardware, in conjunction with the compiler, to assure that the parallel execution does not violate the intent of the program.

## Slide 12
Notes: An alternative approach to achieving greater performance is referred to as super- pipelining, a term first coined in 1988 [JOUP88]. Superpipelining exploits the fact that many pipeline stages perform tasks that require less than half a clock cycle. Thus, a doubled internal clock speed allows the performance of two tasks in one external clock cycle. We have seen one example of this approach with the MIPS R4000.
Figure 16.2 compares the two approaches. The upper part of the diagram illustrates an ordinary pipeline, used as a base for comparison. The base pipeline issues one instruction per clock cycle and can perform one pipeline stage per clock cycle. The pipeline has four stages: instruction fetch, operation decode, operation execution, and result write back. The execution stage is crosshatched for clarity. Note that although several instructions are executing concurrently, only one instruction is in its execution stage at any one time.
The next part of the diagram shows a superpipelined implementation that is capable of performing two pipeline stages per clock cycle. An alternative way of looking at this is that the functions performed in each stage can be split into two non-overlapping parts and each can execute in half a clock cycle. A superpipeline implementation that behaves in this fashion is said to be of degree 2. Finally, the lowest part of the diagram shows a superscalar implementation capable of executing two instances of each stage in parallel. Higher-degree superpipeline and super- scalar implementations are of course possible.
Both the superpipeline and the superscalar implementations depicted in Figure 16.2 have the same number of instructions executing at the same time in the steady state. The superpipelined processor falls behind the superscalar processor at the start of the program and at each branch target.

## Slide 13
Table 15.1
Characteristics of Some CISCs, RISCs, and Superscalar Processors
(Table can be found on page 538 in the textbook.)
Notes: Table 15.1 compares several RISC and non-RISC systems.

## Slide 14
Table 15.1
Characteristics of Some CISCs, RISCs, and Superscalar Processors
(Table can be found on page 538 in the textbook.)
Notes: Table 15.1 compares several RISC and non-RISC systems.

## Slide 15: Instruction Execution Characteristics
High-level languages (HLLs)
Allow the programmer to express algorithms more concisely
Allow the compiler to take care of details that are not important in the programmer’s expression of algorithms
Often support naturally the use of structured programming and/or object-oriented design
Semantic gap
The difference between the operations provided in HLLs and those provided in computer architecture
Operations performed
Determine the functions to be performed by the processor and its interaction with memory
Operands used
The types of operands and the frequency of their use determine the memory organization for storing them and the addressing modes for accessing them
Execution sequencing
Determines the control and pipeline organization
Notes: One of the most visible forms of evolution associated with computers is that of programming languages. As the cost of hardware has dropped, the relative cost of soft- ware has risen. Along with that, a chronic shortage of programmers has driven up software costs in absolute terms. Thus, the major cost in the life cycle of a system is software, not hardware. Adding to the cost, and to the inconvenience, is the element of unreliability: it is common for programs, both system and application, to continue to exhibit new bugs after years of operation.
The response from researchers and industry has been to develop ever more powerful and complex high-level programming languages. These high-level languages (HLLs): (1) allow the programmer to express algorithms more concisely, (2) allow the compiler to take care of details that are not important in the programmer’s expression of algorithms, and (3) often support naturally the use of structured programming and/or object-oriented design.
Alas, this solution gave rise to a perceived problem, known as the semantic gap, the difference between the operations provided in HLLs and those provided in computer architecture. Symptoms of this gap are alleged to include execution inefficiency, excessive machine program size, and compiler complexity. Designers responded with architectures intended to close this gap. Key features include large instruction sets, dozens of addressing modes, and various HLL statements implemented in hardware. An example of the latter is the CASE machine instruction on the VAX. Such complex instruction sets are intended to
  Ease the task of the compiler writer.
  Improve execution efficiency, because complex sequences of operations can
  be implemented in microcode.
  Provide support for even more complex and sophisticated HLLs.
  Meanwhile, a number of studies have been done over the years to determine the characteristics and patterns of execution of machine instructions generated from HLL programs. The results of these studies inspired some researchers to look for a different approach: namely, to make the architecture that supports the HLL simpler, rather than more complex.
To understand the line of reasoning of the RISC advocates, we begin with a brief review of instruction execution characteristics. The aspects of computation of interest are as follows:
Operations performed: These determine the functions to be performed by the processor and its interaction with memory.
Operands used: The types of operands and the frequency of their use deter- mine the memory organization for storing them and the addressing modes for accessing them.
Execution sequencing: This determines the control and pipeline organization.
In the remainder of this section, we summarize the results of a number of studies of high-level-language programs. All of the results are based on dynamic measurements. That is, measurements are collected by executing the program and counting the number of times some feature has appeared or a particular property has held true. In contrast, static measurements merely perform these counts on the source text of a program. They give no useful information on performance, because they are not weighted relative to the number of times each statement is executed.

## Slide 16: Implications
HLLs can best be supported by optimizing performance of the most time-consuming features of typical HLL programs
Three elements characterize RISC architectures:
  Use a large number of registers or use a compiler to optimize register usage
  Careful attention needs to be paid to the design of instruction pipelines
  Instructions should have predictable costs and be consistent with a high-performance implementation
Notes: A number of groups have looked at results such as those just reported and have concluded that the attempt to make the instruction set architecture close to HLLs is not the most effective design strategy. Rather, the HLLs can best be supported by optimizing performance of the most time-consuming features of typical HLL programs.
Generalizing from the work of a number of researchers, three elements emerge that, by and large, characterize RISC architectures. First, use a large number of registers or use a compiler to optimize register usage. This is intended to optimize operand referencing. The studies just discussed show that there are several references per HLL statement and that there is a high proportion of move (assignment) statements. This, coupled with the locality and predominance of scalar references, suggests that performance can be improved by reducing memory references at the expense of more register references. Because of the locality of these references, an expanded register set seems practical.
Second, careful attention needs to be paid to the design of instruction pipe- lines. Because of the high proportion of conditional branch and procedure call instructions, a straightforward instruction pipeline will be inefficient. This manifests itself as a high proportion of instructions that are prefetched but never executed.
Finally, an instruction set consisting of high-performance primitives is indicated. Instructions should have predictable costs (measured in execution time and code size, and increasingly, in energy dissipation) and be consistent with a high-performance implementation (which harmonizes with predictable execution-time cost).

## Slide 17: The Use of a Large Register File
  Requires compiler to allocate registers
  Allocates based on most used variables in a given time
  Requires sophisticated program analysis
  More registers
  Thus more variables will be in registers
Software Solution
Hardware Solution
Notes: The reason that register storage is indicated is that it is the fastest avail- able storage device, faster than both main memory and cache. The register file is physically small, on the same chip as the ALU and control unit, and employs much shorter addresses than addresses for cache and memory. Thus, a strategy is needed that will allow the most frequently accessed operands to be kept in registers and to minimize register-memory operations.
Two basic approaches are possible, one based on software and the other on hardware. The software approach is to rely on the compiler to maximize register usage. The compiler will attempt to assign registers to those variables that will be used the most in a given time period. This approach requires the use of sophisticated program-analysis algorithms. The hardware approach is simply to use more registers so that more variables can be held in registers for longer periods of time.

## Slide 18
Notes: On the face of it, the use of a large set of registers should decrease the need to access memory. The design task is to organize the registers in such a fashion that this goal is realized.
Because most operand references are to local scalars, the obvious approach is to store these in registers, with perhaps a few registers reserved for global variables. The problem is that the definition of local changes with each procedure call and return, operations that occur frequently. On every call, local variables must be saved from the registers into memory, so that the registers can be reused by the called procedure. Furthermore, parameters must be passed. On return, the variables of the calling procedure must be restored (loaded back into registers) and results must be passed back to the calling procedure.
The solution is based on two other results reported in Section 15.1. First, a typical procedure employs only a few passed parameters and local variables (Table 15.4). Second, the depth of procedure activation fluctuates within a relatively narrow range (Figure 4.21). To exploit these properties, multiple small sets of registers are used, each assigned to a different procedure. A procedure call automatically switches the processor to use a different fixed-size window of registers, rather than saving registers in memory. Windows for adjacent procedures are overlapped to allow parameter passing.
The concept is illustrated in Figure 15.1. At any time, only one window of registers is visible and is addressable as if it were the only set of registers (e.g., addresses 0 through N - 1). The window is divided into three fixed-size areas. Parameter registers hold parameters passed down from the procedure that called the current procedure and hold results to be passed back up. Local registers are used for local variables, as assigned by the compiler. Temporary registers are used to exchange parameters and results with the next lower level (procedure called by current procedure). The temporary registers at one level are physically the same as the parameter registers at the next lower level. This overlap permits parameters to be passed without the actual movement of data. Keep in mind that, except for the overlap, the registers at two different levels are physically distinct. That is, the parameter and local registers at level J are disjoint from the local and temporary registers at level J + 1.
To handle any possible pattern of calls and returns, the number of register windows would have to be unbounded. Instead, the register windows can be used to hold the few most recent procedure activations. Older activations must be saved
in memory and later restored when the nesting depth decreases. Thus, the actual organization of the register file is as a circular buffer of overlapping windows. Two notable examples of this approach are Sun’s SPARC architecture, described in Section 15.7, and the IA-64 architecture used in Intel’s Itanium processor.

## Slide 19
Notes: The circular organization is shown in Figure 15.2, which depicts a circular buffer of six windows. The buffer is filled to a depth of 4 (A called B; B called C; C called D) with procedure D active. The current-window pointer (CWP) points to the window of the currently active procedure. Register references by a machine instruction are offset by this pointer to determine the actual physical register. The saved-window pointer (SWP) identifies the window most recently saved in memory. If procedure D now calls procedure E, arguments for E are placed in D’s temporary registers (the overlap between w3 and w4) and the CWP is advanced by one window.
If procedure E then makes a call to procedure F, the call cannot be made with the current status of the buffer. This is because F’s window overlaps A’s window. If F begins to load its temporary registers, preparatory to a call, it will overwrite the parameter registers of A (A.in). Thus, when CWP is incremented (modulo 6) so that it becomes equal to SWP, an interrupt occurs, and A’s window is saved. Only the first two portions (A.in and A.loc) need be saved. Then, the SWP is incremented and the call to F proceeds. A similar interrupt can occur on returns. For example, subsequent to the activation of F, when B returns to A, CWP is decremented and becomes equal to SWP. This causes an interrupt that results in the restoration of A’s window.
From the preceding, it can be seen that an N-window register file can hold only N - 1 procedure activations. The value of N need not be large. As was mentioned in Appendix 4A, one study [TAMI83] found that, with 8 windows, a save or restore is needed on only 1% of the calls or returns. The Berkeley RISC computers use 8 windows of 16 registers each. The Pyramid computer employs 16 windows of 32 registers each.

## Slide 20
Table 15.5
Characteristics of Large-Register-File
and Cache Organizations
(Table can be found on page 546 in the textbook.)
Notes: The register file, organized into windows, acts as a small, fast buffer for holding a subset of all variables that are likely to be used the most heavily. From this point of view, the register file acts much like a cache memory, although a much faster memory. The question therefore arises as to whether it would be simpler and better to use a cache and a small traditional register file.
Table 15.5 compares characteristics of the two approaches. The window-based register file holds all the local scalar variables (except in the rare case of window overflow) of the most recent N - 1 procedure activations. The cache holds a selection of recently used scalar variables. The register file should save time, because all local scalar variables are retained. On the other hand, the cache may make more efficient use of space, because it is reacting to the situation dynamically. Furthermore, caches generally treat all memory references alike, including instructions and other types of data. Thus, savings in these other areas are possible with a cache and not a register file.
A register file may make inefficient use of space, because not all procedures will need the full window space allotted to them. On the other hand, the cache suffers from another sort of inefficiency: Data are read into the cache in blocks. Whereas the register file contains only those variables in use, the cache reads in a block of data, some or much of which will not be used.
The cache is capable of handling global as well as local variables. There are usually many global scalars, but only a few of them are heavily used [KATE83]. A cache will dynamically discover these variables and hold them. If the window- based register file is supplemented with global registers, it too can hold some global scalars. However, when program modules are separately compiled, it is impossible for the compiler to assign global values to registers; the linker must perform this task.
With the register file, the movement of data between registers and memory is determined by the procedure nesting depth. Because this depth usually fluctuates within a narrow range, the use of memory is relatively infrequent. Most cache memories are set associative with a small set size. Thus, there is the danger that other data or instructions will compete for cache residency.

## Slide 21: Why CISC ?
  There is a trend to richer instruction sets which include a larger and more complex number of instructions
  Two principal reasons for this trend:
  A desire to simplify compilers
  A desire to improve performance
  There are two advantages to smaller programs:
  The program takes up less memory
  Should improve performance
    Fewer instructions means fewer instruction bytes to be fetched
    In a paging environment smaller programs occupy fewer pages, reducing page faults
    More instructions fit in cache(s)
(Complex Instruction Set Computer)
Notes: We have noted the trend to richer instruction sets, which include a larger number of instructions and more complex instructions. Two principal reasons have motivated this trend: a desire to simplify compilers and a desire to improve performance. Underlying both of these reasons was the shift to HLLs on the part of programmers; architects attempted to design machines that provided better support for HLLs.
It is not the intent of this chapter to say that the CISC designers took the wrong direction. Indeed, because technology continues to evolve and because architectures exist along a spectrum rather than in two neat categories, a black-and-white assessment is unlikely ever to emerge. Thus, the comments that follow are simply meant to point out some of the potential pitfalls in the CISC approach and to pro- vide some understanding of the motivation of the RISC adherents.
The first of the reasons cited, compiler simplification, seems obvious, but it is not. The task of the compiler writer is to build a compiler that generates good (fast, small, fast and small) sequences of machine instructions for HLL programs (i.e., the compiler views individual HLL statements in the context of surrounding HLL statements). If there are machine instructions that resemble HLL statements, this task is simplified. This reasoning has been disputed by the RISC researchers ([HENN82], [RADI83], [PATT82b]). They have found that complex machine instructions are often hard to exploit because the compiler must find those cases that exactly fit the construct. The task of optimizing the generated code to minimize code size, reduce instruction execution count, and enhance pipelining is much more difficult with a complex instruction set. As evidence of this, studies cited earlier in this chapter indicate that most of the instructions in a compiled program are the relatively simple ones.
The other major reason cited is the expectation that a CISC will yield smaller, faster programs. Let us examine both aspects of this assertion: that programs will be smaller and that they will execute faster.
There are two advantages to smaller programs. First, because the program takes up less memory, there is a savings in that resource. With memory today being so inexpensive, this potential advantage is no longer compelling. More important, smaller programs should improve performance, and this will happen in three ways. First, fewer instructions means fewer instruction bytes to be fetched. Second, in a paging environment, smaller programs occupy fewer pages, reducing page faults. Third, more instructions fit in cache(s).

## Slide 22
Table 15.6
Code Size Relative to RISC I
(Table can be found on page 550 in the textbook.)
Notes: The problem with this line of reasoning is that it is far from certain that a CISC program will be smaller than a corresponding RISC program. In many cases, the CISC program, expressed in symbolic machine language, may be shorter (i.e., fewer instructions), but the number of bits of memory occupied may not be noticeably smaller. Table 15.6 shows results from three studies that compared the size of com- piled C programs on a variety of machines, including RISC I, which has a reduced instruction set architecture. Note that there is little or no savings using a CISC over a RISC. It is also interesting to note that the VAX, which has a much more complex instruction set than the PDP-11, achieves very little savings over the latter. These results were confirmed by IBM researchers [RADI83], who found that the IBM 801 (a RISC) produced code that was 0.9 times the size of code on an IBM S/370. The study used a set of PL/I programs.
There are several reasons for these rather surprising results. We have already noted that compilers on CISCs tend to favor simpler instructions, so that the conciseness of the complex instructions seldom comes into play. Also, because there are more instructions on a CISC, longer opcodes are required, producing longer instructions. Finally, RISCs tend to emphasize register rather than memory references, and the former require fewer bits. An example of this last effect is discussed presently.
So the expectation that a CISC will produce smaller programs, with the attend- ant advantages, may not be realized. The second motivating factor for increasingly complex instruction sets was that instruction execution would be faster. It seems to make sense that a complex HLL operation will execute more quickly as a single machine instruction rather than as a series of more primitive instructions. However, because of the bias toward the use of those simpler instructions, this may not be so.
The entire control unit must be made more complex, and/or the microprogram control store must be made larger, to accommodate a richer instruction set. Either factor increases the execution time of the simple instructions.
In fact, some researchers have found that the speedup in the execution of complex functions is due not so much to the power of the complex machine instructions as to their residence in high-speed control store [RADI83]. In effect, the control store acts as an instruction cache. Thus, the hardware architect is in the position of trying to determine which subroutines or functions will be used most frequently and assigning those to the control store by implementing them in microcode. The results have been less than encouraging. On S/390 systems, instructions such as Translate and Extended-Precision-Floating-Point-Divide reside in high-speed storage, while the sequence involved in setting up procedure calls or initiating an interrupt handler are in slower main memory.
Thus, it is far from clear that a trend to increasingly complex instruction sets is appropriate. This has led a number of groups to pursue the opposite path.

## Slide 23: Characteristics of Reduced Instruction Set Architectures
One machine instruction per machine cycle
Machine cycle --- the time it takes to fetch two operands from registers, perform an ALU operation, and store the result in a register
Register-to-register operations
Only simple LOAD and STORE operations accessing memory
This simplifies the instruction set and therefore the control unit
Simple addressing modes
Simplifies the instruction set and the control unit
Simple instruction formats
Generally only one or a few formats are used
Instruction length is fixed and aligned on word boundaries
Opcode decoding and register operand accessing can occur simultaneously
Notes: Although a variety of different approaches to reduced instruction set architecture have been taken, certain characteristics are common to all of them:
• One instruction per cycle
• Register-to-register operations
• Simple addressing modes
• Simple instruction formats
Here, we provide a brief discussion of these characteristics. Specific examples are explored later in this chapter.
The first characteristic listed is that there is one machine instruction per machine cycle. A machine cycle is defined to be the time it takes to fetch two operands from registers, perform an ALU operation, and store the result in a register. Thus, RISC machine instructions should be no more complicated than, and execute about as fast as, microinstructions on CISC machines (discussed in Part Four). With simple, one-cycle instructions, there is little or no need for microcode; the machine instructions can be hardwired. Such instructions should execute faster than comparable machine instructions on other machines, because it is not necessary to access a microprogram control store during instruction execution.
A second characteristic is that most operations should be register to register, with only simple LOAD and STORE operations accessing memory. This design feature simplifies the instruction set and therefore the control unit. For example, a RISC instruction set may include only one or two ADD instructions (e.g., integer add, add with carry); the VAX has 25 different ADD instructions. Another benefit is that such an architecture encourages the optimization of register use, so that frequently accessed operands remain in high-speed storage.
A third characteristic is the use of simple addressing modes. Almost all RISC instructions use simple register addressing. Several additional modes, such as displacement and PC-relative, may be included. Other, more complex modes can be synthesized in software from the simple ones. Again, this design feature simplifies the instruction set and the control unit.
A final common characteristic is the use of simple instruction formats. Generally, only one or a few formats are used. Instruction length is fixed and aligned on word boundaries. Field locations, especially the opcode, are fixed. This design feature has a number of benefits. With fixed fields, opcode decoding and register operand accessing can occur simultaneously. Simplified formats simplify the control unit. Instruction fetching is optimized because word-length units are fetched. Alignment on a word boundary also means that a single instruction does not cross page boundaries.

## Slide 24
Table 15.7
Characteristics of Some Processors
(Table can be found on page 554 in the textbook.)
Notes: After the initial enthusiasm for RISC machines, there has been a growing realization
that (1) RISC designs may benefit from the inclusion of some CISC features and that
(2) CISC designs may benefit from the inclusion of some RISC features. The result is
that the more recent RISC designs, notably the PowerPC, are no longer “pure” RISC
and the more recent CISC designs, notably the Pentium II and later Pentium models,
do incorporate some RISC characteristics.
An interesting comparison in [MASH95] provides some insight into this issue. Table 15.7 lists a number of processors and compares them across a number of characteristics. For purposes of this comparison, the following are considered typical of a classic RISC:
A single instruction size.
That size is typically 4 bytes.
A small number of data addressing modes, typically less than five. This parameter is difficult to pin down. In the table, register and literal modes are not counted and different formats with different offset sizes are counted separately.
No indirect addressing that requires you to make one memory access to get
the address of another operand in memory.
No operations that combine load/store with arithmetic (e.g.,add from memory, add to memory).
No more than one memory-addressed operand per instruction.
Does not support arbitrary alignment of data for load/store operations.
Maximum number of uses of the memory management unit (MMU) for a data address in an instruction.
Number of bits for integer register specifier equal to five or more. This means that at least 32 integer registers can be explicitly referenced at a time.
Number of bits for floating-point register specifier equal to four or more. This means that at least 16 floating-point registers can be explicitly referenced at a time.
Items 1 through 3 are an indication of instruction decode complexity. Items 4
through 8 suggest the ease or difficulty of pipelining, especially in the presence of virtual memory requirements. Items 9 and 10 are related to the ability to take good advantage of compilers.
In the table, the first eight processors are clearly RISC architectures, the next five are clearly CISC, and the last two are processors often thought of as RISC that in fact have many CISC characteristics.

## Slide 25: Optimization of Pipelining
Delayed branch
  Does not take effect until after execution of following instruction
  This following instruction is the delay slot
Delayed Load
  Register to be target is locked by processor
  Continue execution of instruction stream until register required
  Idle until load is complete
  Re-arranging instructions can allow useful work while loading
Loop Unrolling
  Replicate body of loop a number of times
  Iterate loop fewer times
  Reduces loop overhead
  Increases instruction parallelism
  Improved register, data cache, or TLB locality
Notes: Because of the simple and regular nature of RISC instructions, it is easier for a hardware designer to implement a simple, fast pipeline. There are few variations in instruction execution duration, and the pipeline can be tailored to reflect this. However, we have seen that data and branch dependencies reduce the overall execution rate.
To compensate for these dependencies, code reorganization techniques have been developed.

## Slide 26
Table 15.8
Normal And Delayed Branch
(Table can be found on page 557 in the textbook.)
Notes: First, let us consider branching instructions. Delayed branch, a way of increasing the efficiency of the pipeline, makes use of a branch that does not take effect until after execution of the following instruction (hence the term delayed). The instruction location immediately following the branch is referred to as the delay slot. This strange procedure is illustrated in Table 15.8. In the column labeled “normal branch,” we see a normal symbolic instruction machine-language program. After 102 is executed, the next instruction to be executed is 105. To regularize the pipeline, a NOOP is inserted after this branch. However, increased performance is achieved if the instructions at 101 and 102 are interchanged.

## Slide 27
Notes: Figure 15.7 shows the result. Figure 15.7a shows the traditional approach to pipelining, of the type discussed in Chapter 14 (e.g., see Figures 14.11 and 14.12). The JUMP instruction is fetched at time 3. At time 4, the JUMP instruction is executed at the same time that instruction 103 (ADD instruction) is fetched. Because a JUMP occurs, which updates the program counter, the pipeline must be cleared of instruction 103; at time 5, instruction 105, which is the target of the JUMP, is loaded. Figure 15.7b shows the same pipeline handled by a typical RISC organization. The timing is the same. However, because of the insertion of the NOOP instruction, we do not need special circuitry to clear the pipeline; the NOOP simply executes with no effect. Figure 15.7c shows the use of the delayed branch. The JUMP instruction is fetched at time 2, before the ADD instruction, which is fetched at time 3. Note, however, that the ADD instruction is fetched before the execution of the JUMP instruction has a chance to alter the program counter. Therefore, during time 4, the ADD instruction is executed at the same time that instruction 105 is fetched.
Thus, the original semantics of the program are retained but one less clock cycle is required for execution.
This interchange of instructions will work successfully for unconditional branches, calls, and returns. For conditional branches, this procedure cannot be blindly applied. If the condition that is tested for the branch can be altered by the immediately preceding instruction, then the compiler must refrain from doing the interchange and instead insert a NOOP. Otherwise, the compiler can seek to insert a useful instruction after the branch. The experience with both the Berkeley RISC and IBM 801 systems is that the majority of conditional branch instructions can be optimized in this fashion ([PATT82a], [RADI83]).
A similar sort of tactic, called the delayed load, can be used on LOAD instructions. On LOAD instructions, the register that is to be the target of the load is locked by the processor. The processor then continues execution of the instruction stream until it reaches an instruction requiring that register, at which point it idles until the load is complete. If the compiler can rearrange instructions
so that useful work can be done while the load is in the pipeline, efficiency is
increased.

## Slide 28: RISC versus CISC Controversy
Quantitative
  Compare program sizes and execution speeds of programs on RISC and CISC machines that use comparable technology
Qualitative
  Examine issues of high level language support and use of VLSI real estate
Problems with comparisons:
  No pair of RISC and CISC machines that are comparable in life-cycle cost, level of technology, gate complexity, sophistication of compiler, operating system support, etc.
  No definitive set of test programs exists
  Difficult to separate hardware effects from complier effects
  Most comparisons done on “toy” rather than commercial products
  Most commercial devices advertised as RISC possess a mixture of RISC and CISC characteristics
Notes: For many years, the general trend in computer architecture and organization has been toward increasing processor complexity: more instructions, more addressing modes, more specialized registers, and so on. The RISC movement represents a fundamental break with the philosophy behind that trend. Naturally, the appearance of RISC systems, and the publication of papers by its proponents extolling RISC virtues, led to a reaction from those involved in the design of CISC architectures.
The work that has been done on assessing merits of the RISC approach can be grouped into two categories:
Quantitative: Attempts to compare program size and execution speed of pro- grams on RISC and CISC machines that use comparable technology
Qualitative: Examines issues such as high-level language support and optimum use of VLSI real estate
Most of the work on quantitative assessment has been done by those working on RISC systems [PATT82b, HEAT84, PATT84], and it has been, by and large, favorable to the RISC approach. Others have examined the issue and come away unconvinced [COLW85a, FLYN87, DAVI87]. There are several problems with attempting such comparisons [SERL86]:
There is no pair of RISC and CISC machines that are comparable in life-cycle cost, level of technology, gate complexity, sophistication of compiler, operating system support, and so on.
No definitive test set of programs exists. Performance varies with the program.
It is difficult to sort out hardware effects from effects due to skill in compiler
writing.
Most of the comparative analysis on RISC has been done on “toy” machines rather than commercial products. Furthermore, most commercially available machines advertised as RISC possess a mixture of RISC and CISC characteristics. Thus, a fair comparison with a commercial, “pure-play” CISC machine (e.g., VAX, Pentium) is difficult.
The qualitative assessment is, almost by definition, subjective. Several researchers
have turned their attention to such an assessment [COLW85a, WALL85], but
the results are, at best, ambiguous, and certainly subject to rebuttal [PATT85b] and,
of course, counterrebuttal [COLW85b].
In more recent years, the RISC versus CISC controversy has died down to
a great extent. This is because there has been a gradual convergence of the technologies.
As chip densities and raw hardware speeds increase, RISC systems have
become more complex. At the same time, in an effort to squeeze out maximum performance,
CISC designs have focused on issues traditionally associated with RISC,
such as an increased number of general-purpose registers and increased emphasis
on instruction pipeline design.

## Slide 29: Chapter 17
Parallel Processing
Notes: Traditionally, the computer has been viewed as a sequential machine. Most computer programming languages require the programmer to specify algorithms as sequences of instructions. Processors execute programs by executing machine instructions in a sequence and one at a time. Each instruction is executed in a sequence of operations (fetch instruction, fetch operands, perform operation, store results).
This view of the computer has never been entirely true. At the micro-operation level, multiple control signals are generated at the same time. Instruction pipelining, at least to the extent of overlapping fetch and execute operations, has been around for a long time. Both of these are examples of performing functions in parallel. This approach is taken further with superscalar organization, which exploits instruction- level parallelism. With a superscalar machine, there are multiple execution units within a single processor, and these may execute multiple instructions from the same program in parallel.
As computer technology has evolved, and as the cost of computer hardware
has dropped, computer designers have sought more and more opportunities
for parallelism, usually to enhance performance and, in some cases, to increase
availability. After an overview, this chapter looks at some of the most prominent
approaches to parallel organization. First, we examine symmetric multiprocessors
(SMPs), one of the earliest and still the most common example of parallel
organization. In an SMP organization, multiple processors share a common
memory. This organization raises the issue of cache coherence, to which a separate
section is devoted. Next, the chapter examines multithreaded processors
and chip multiprocessors. Then we describe clusters, which consist of multiple
independent computers organized in a cooperative fashion. Clusters have become
increasingly common to support workloads that are beyond the capacity of a
single SMP. Another approach to the use of multiple processors that we examine
is that of nonuniform memory access (NUMA) machines. The NUMA approach
is relatively new and not yet proven in the marketplace, but is often considered as
an alternative to the SMP or cluster approach. Finally, this chapter looks at cloud
computing architecture.

## Slide 30: Multiple Processor Organization
Single instruction, single data (SISD) stream
  Single processor executes a single instruction stream to operate on data stored in a single memory
  Uniprocessors fall into this category
Single instruction, multiple data (SIMD) stream
  A single machine instruction controls the simultaneous execution of a number of processing elements on a lockstep basis
  Vector and array processors fall into this category
Multiple instruction, single data (MISD) stream
  A sequence of data is transmitted to a set of processors, each of which executes a different instruction sequence
  Not commercially implemented
Multiple instruction, multiple data (MIMD) stream
  A set of processors simultaneously execute different instruction sequences on different data sets
  SMPs, clusters and NUMA systems fit this category
Notes: A taxonomy first introduced by Flynn [FLYN72] is still the most common way of categorizing systems with parallel processing capability. Flynn proposed the following categories of computer systems:
Single instruction, single data (SISD) stream: A single processor executes a single instruction stream to operate on data stored in a single memory. Uniprocessors fall into this category.
Single instruction, multiple data (SIMD) stream: A single machine instruction controls the simultaneous execution of a number of processing elements on a lockstep basis. Each processing element has an associated data memory, so that instructions are executed on different sets of data by different processors. Vector and array processors fall into this category, and are discussed in Section 18.7.
Multiple instruction, single data (MISD) stream: A sequence of data is transmitted to a set of processors, each of which executes a different instruction sequence. This structure is not commercially implemented.
Multiple instruction, multiple data (MIMD) stream: A set of processors simultaneously execute different instruction sequences on different data sets. SMPs, clusters, and NUMA systems fit into this category.

## Slide 31
Notes: With the MIMD organization, the processors are general purpose; each is able to process all of the instructions necessary to perform the appropriate data transformation. MIMDs can be further subdivided by the means in which the processors communicate (Figure 17.1). If the processors share a common memory, then each processor accesses programs and data stored in the shared memory, and processors communicate with each other via that memory. The most common form of such system is known as a symmetric multiprocessor (SMP), which we examine in Section 17.2. In an SMP, multiple processors share a single memory or pool of memory by means of a shared bus or other interconnection mechanism; a distinguishing feature is that the memory access time to any region of memory is approximately the same for each processor. A more recent development is the non-uniform memory access (NUMA) organization, which is described in Section 17.5. As the name suggests, the memory access time to different regions of memory may differ for a NUMA processor.
A collection of independent uniprocessors or SMPs may be interconnected to form a cluster. Communication among the computers is either via fixed paths or via some network facility.

## Slide 32
Notes: Figure 17.2 illustrates the general organization of the taxonomy of Figure 17.1. Figure 17.2a shows the structure of an SISD. There is some sort of control unit (CU) that provides an instruction stream (IS) to a processing unit (PU). The processing unit operates on a single data stream (DS) from a memory unit (MU). With an
SIMD, there is still a single control unit, now feeding a single instruction stream to multiple PUs. Each PU may have its own dedicated memory (illustrated in Figure 17.2b), or there may be a shared memory. Finally, with the MIMD, there are multiple control units, each feeding a separate instruction stream to its own PU. The MIMD may be a shared-memory multiprocessor (Figure 17.2c) or a distributed- memory multicomputer (Figure 17.2d).
The design issues relating to SMPs, clusters, and NUMAs are complex, involving issues relating to physical organization, interconnection structures, inter-processor communication, operating system design, and application software techniques. Our concern here is primarily with organization, although we touch briefly on operating system design issues.

## Slide 33: Symmetric Multiprocessor (SMP)
A stand alone computer with the following characteristics:
Two or more similar processors of comparable capacity
Processors share same memory and I/O facilities
Processors are connected by a bus or other internal connection
Memory access time is approximately the same for each processor
All processors share access to I/O devices
Either through same channels or different channels giving paths to same devices
All processors can perform the same functions (hence “symmetric”)
System controlled by integrated operating system
Provides interaction between processors and their programs at job, task, file and data element levels
Notes: Until fairly recently, virtually all single-user personal computers and most workstations contained a single general-purpose microprocessor. As demands for performance increase and as the cost of microprocessors continues to drop, vendors have introduced systems with an SMP organization. The term SMP refers to a computer hardware architecture and also to the operating system behavior that reflects that architecture. An SMP can be defined as a standalone computer system with the following characteristics:
1. There are two or more similar processors of comparable capability.
2. These processors share the same main memory and I/O facilities and are interconnected by a bus or other internal connection scheme, such that memory access time is approximately the same for each processor.
3. All processors share access to I/O devices, either through the same channels or through different channels that provide paths to the same device.
4. All processors can perform the same functions (hence the term symmetric).
5. The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and data element levels.
Points 1 to 4 should be self-explanatory. Point 5 illustrates one of the contrasts
with a loosely coupled multiprocessing system, such as a cluster. In the latter, the physical unit of interaction is usually a message
or complete file. In an SMP, individual data elements can constitute the level of interaction, and there can be a high degree of cooperation
between processes.

## Slide 34
Notes: Figure 17.4 depicts in general terms the organization of a multiprocessor system. There are two or more processors. Each processor is self-contained, including a control unit, ALU, registers, and, typically, one or more levels of cache. Each processor has access to a shared main memory and the I/O devices through some form of interconnection mechanism. The processors can communicate with each other through memory (messages and status information left in common data areas). It may also be possible for processors to exchange signals directly. The memory is often organized so that multiple simultaneous accesses to separate blocks of memory are possible. In some configurations, each processor may also have its own private main memory and I/O channels in addition to the shared resources.

## Slide 35
Notes: The most common organization for personal computers, workstations, and servers is the time-shared bus. The time-shared bus is the simplest mechanism for constructing a multiprocessor system (Figure 17.5). The structure and interfaces are basically the same as for a single-processor system that uses a bus interconnection. The bus consists of control, address, and data lines. To facilitate DMA transfers from I/O subsystems to processors, the following features are provided:
Addressing: It must be possible to distinguish modules on the bus to determine the source and destination of data.
Arbitration: Any I/O module can temporarily function as “master.” A mechanism is provided to arbitrate competing requests for bus control, using some sort of priority scheme.
Time-sharing: When one module is controlling the bus, other modules are locked out and must, if necessary, suspend operation until bus access is achieved.
These uniprocessor features are directly usable in an SMP organization. In this latter case, there are now multiple processors as well as multiple I/O processors all attempting to gain access to one or more memory modules via the bus.

## Slide 36: Clusters
Alternative to SMP as an approach to providing high performance and high availability
Particularly attractive for server applications
Defined as:
  A group of interconnected whole computers working together as a unified computing resource that can create the illusion of being one machine
  (The term whole computer means a system that can run on its own, apart from the cluster)
Each computer in a cluster is called a node
Benefits:
  Absolute scalability
  Incremental scalability
  High availability
  Superior price/performance
Notes: An important and relatively recent development computer system design is clustering. Clustering is an alternative to symmetric multiprocessing as an approach to providing high performance and high availability and is particularly attractive for server applications. We can define a cluster as a group of interconnected, whole computers working together as a unified computing resource that can create the illusion of being one machine. The term whole computer means a system that can run on its own, apart from the cluster; in the literature, each computer in a cluster is typically referred to as a node.
[BREW97] lists four benefits that can be achieved with clustering. These can also be thought of as objectives or design requirements:
• Absolute scalability: It is possible to create large clusters that far surpass the power of even the largest standalone machines. A cluster can have tens, hundreds, or even thousands of machines, each of which is a multiprocessor.
• Incremental scalability: A cluster is configured in such a way that it is possible to add new systems to the cluster in small increments. Thus, a user can start out with a modest system and expand it as needs grow, without having to go through a major upgrade in which an existing small system is replaced with a larger system.
• High availability: Because each node in a cluster is a standalone computer, the failure of one node does not mean loss of service. In many products, fault tolerance is handled automatically in software.
• Superior price/performance: By using commodity building blocks, it is possible to put together a cluster with equal or greater computing power than a single large machine, at much lower cost.

## Slide 37
Notes: In the literature, clusters are classified in a number of different ways. Perhaps the simplest classification is based on whether the computers in a cluster share access to the same disks. Figure 17.8a shows a two-node cluster in which the only interconnection is by means of a high-speed link that can be used for message exchange to coordinate cluster activity. The link can be a LAN that is shared with other computers that are not part of the cluster or the link can be a dedicated interconnection facility. In the latter case, one or more of the computers in the cluster will have a link to a LAN or WAN so that there is a connection between the server cluster and remote client systems. Note that in the figure, each computer is depicted as being a multiprocessor. This is not necessary but does enhance both performance and availability.
In the simple classification depicted in Figure 17.8, the other alternative is a shared-disk cluster. In this case, there generally is still a message link between
nodes. In addition, there is a disk subsystem that is directly linked to multiple computers within the cluster. In this figure, the common disk subsystem is a RAID system. The use of RAID or some similar redundant disk technology is common in clusters so that the high availability achieved by the presence of multiple computers is not compromised by a shared disk that is a single point of failure.
A common, older method, known as passive standby , is simply to have one
computer handle all of the processing load while the other computer remains
inactive, standing by to take over in the event of a failure of the primary. To coordinate
the machines, the active, or primary, system periodically sends a “heartbeat”
message to the standby machine. Should these messages stop arriving, the standby
assumes that the primary server has failed and puts itself into operation. This
approach increases availability but does not improve performance. Further, if the
only information that is exchanged between the two systems is a heartbeat message,
and if the two systems do not share common disks, then the standby provides a
functional backup but has no access to the databases managed by the primary.
The passive standby is generally not referred to as a cluster. The term cluster
is reserved for multiple interconnected computers that are all actively doing processing
while maintaining the image of a single system to the outside world. The
term active secondary is often used in referring to this configuration. Three classifications
of clustering can be identified: separate servers, shared nothing, and shared
memory.
In one approach to clustering, each computer is a separate server with its own
disks and there are no disks shared between systems (Figure 17.8a). This arrangement
provides high performance as well as high availability. In this case, some type
of management or scheduling software is needed to assign incoming client requests
to servers so that the load is balanced and high utilization is achieved. It is desirable
to have a failover capability, which means that if a computer fails while executing
an application, another computer in the cluster can pick up and complete
the application. For this to happen, data must constantly be copied among systems
so that each system has access to the current data of the other systems. The overhead
of this data exchange ensures high availability at the cost of a performance
penalty.
To reduce the communications overhead, most clusters now consist of servers
connected to common disks (Figure 17.8b). In one variation on this approach, called
shared nothing , the common disks are partitioned into volumes, and each volume is
owned by a single computer. If that computer fails, the cluster must be reconfigured
so that some other computer has ownership of the volumes of the failed computer.
It is also possible to have multiple computers share the same disks at the same
time (called the shared disk approach), so that each computer has access to all of the
volumes on all of the disks. This approach requires the use of some type of locking
facility to ensure that data can only be accessed by one computer at a time.

## Slide 38: Nonuniform Memory Access (NUMA)
Alternative to SMP and clustering
Uniform memory access (UMA)
  All processors have access to all parts of main memory using loads and stores
  Access time to all regions of memory is the same
  Access time to memory for different processors is the same
Nonuniform memory access (NUMA)
  All processors have access to all parts of main memory using loads and stores
  Access time of processor differs depending on which region of main memory is being accessed
  Different processors access different regions of memory at different speeds
Cache-coherent NUMA (CC-NUMA)
  A NUMA system in which cache coherence is maintained among the caches of the various processors
Notes: In terms of commercial products, the two common approaches to providing a multiple-processor system to support applications are SMPs and clusters. For some years, another approach, known as nonuniform memory access (NUMA), has been the subject of research and commercial NUMA products are now available.
Before proceeding, we should define some terms often found in the NUMA literature.
• Uniform memory access (UMA): All processors have access to all parts of main memory using loads and stores. The memory access time of a processor to all regions of memory is the same. The access times experienced by different processors are the same. The SMP organization discussed in Sections 17.2 and 17.3 is UMA.
• Nonuniform memory access (NUMA): All processors have access to all parts of main memory using loads and stores. The memory access time of a processor differs depending on which region of main memory is accessed. The last statement is true for all processors; however, for different processors, which memory regions are slower and which are faster differ.
• Cache-coherent NUMA (CC-NUMA): A NUMA system in which cache coherence is maintained among the caches of the various processors.
A NUMA system without cache coherence is more or less equivalent to a cluster. The commercial products that have received much attention recently are CC-NUMA systems, which are quite distinct from both SMPs and clusters. Usually, but unfortunately not always, such systems are in fact referred to in the commercial literature as CC-NUMA systems.

## Slide 39: Assignment 4.(과제4)
1. Instruction size: 3 bytes, byte addressable, Integer: 8bit twos complement representation
R1 = 70, R2= 80, M[70] = 70, M[71] = 71, M[72] = 72
300: MOV R2, #70 ; R2 <= 70 (immediate addressing)
303: SUB R2, @R1 ; R2 <= R2 - M[R1] (register indirect addressing)
306: JZ $-9 ; branch if zero (branch to -9@PC, relative addressing)
1) After executing MOV and SUB instructions, what value is stored in register R2? Show the calculation of SUB.
2) Show the values of flags (C, Z, S, OV) after SUB instruction.
3) What is the address of the instruction executed after JZ instruction?
2. A pipelined processor has a clock rate of 1GHz and executes a program with ten million instructions.
The pipeline has five stages and instructions are issued at a rate of one per clock.
1) What is the speedup of this processor for this program compared to a non-pipelined processor.
2) What is the MIPS rate for the pipelined and non-pipelined processor.
3) List three pipeline hazards and briefly explain how these hazards affect the performance.
3. Choose all items which are more related with RISC compared to CISC.
① µ-programmed control unit ② various instruction size ③ simple addressing mode
④ x86 processor ⑤ ARM processor ⑥ arithmetic combined with load/store
⑦ large number of registers ⑧ small number of op codes ⑨ control memory
4. Choose all the features of an SMP.
① There are 2 or more similar processors of comparable capability.
② All processors can perform the same functions.
③ Each processor is controlled by each operating system.
④ Memory access time depends on the location of each processor.
⑤ All processors share the same main memory and I/O facilities
5. Show the size of each storage to store the followings, and show their binary representation.
1) character ‘1’, 2) string “1”, 3) integer 1, and 4) real number(single precision) 1.0.

## Slide 40: Notice(유의사항)
이번 학기의 최종 성적 구성은
Final-exam : 60%, Assignments : 20%, Attendance : 20% 입니다.
과제물은 이메일(kscho@dankook.ac.kr)로 제출하며, 파일을 절대 첨부하지 말고 메일 본문에 직접 과제에 대한 답을 적어야 합니다. 이메일의 제목은 반드시 “과제번호-분반-이름-학번”으로 해야 합니다 (예, 과제4-분반1-홍길동-1234567) 이를 지키지 않으면 감점이 됩니다. 월/수요일 1:00-2:30 수업은 분반1, 2:30-4:00 수업은 분반2 이며, 오늘 과제의 번호는 과제4입니다.
기말고사도 동일한 방법으로 풀이를 제출하므로, 과제 제출시에 유의 사항을 반드시 숙지하기 바랍니다.