## Slide 1
Computer Architecture (컴퓨터 구조론)
Dept. of Software Science, Dankook University

## Slide 2
조 경 산 교수:
kscho@dankook.ac.kr (원격 강의 기간 연락처)

## Slide 3
Text:
1. Computer Organization and Architecture. 10th Edition By William Stallings, Pearson
2. 컴퓨터시스템구조론 (10판)
김종현역, 성진미디어

## Slide 4: Topics Covered
4
This course provides a systematic overview of the internal structure and operation of modern computer systems
basics and performance of computer systems
memory systems including caches and virtual memory
I/O operations and interrupt mechanisms
instruction sets, inside the processor(RISC and CISC).
interconnection and bus
Notes: 4

## Slide 5: Grading Policy
5
Penalty for more than one being late/no-attendance
No credit for any missing regular Exams
All assignments are done individually
Final-exam : 60%
Assignments : 20%
Attendance : 20%
Notes: 5

## Slide 6
PPTs are from lecture slides of the following book.
Computer Organization and Architecture 10th Edition By William Stallings, Pearson

## Slide 7: Notice(주의사항) - 1
교과목에 대한 공지 사항은 단국대학교 어플의 알림과 이러닝 캠퍼스 해당 과목의 공지란을 통해 수시로 통보됩니다. ==>> 주기적으로 확인 필요합니다.
교과목 및 수업에 관한 모든 질문은 이메일(kscho@dankook.ac.kr)을 통해서 받습니다.
<수업 관련>
수업은 원격 수업으로 주단위로 진행되며, 주 단위의 강의 자료와 원격 강의 동영상은 매주 월요일 13:00에 이러닝 캠퍼스 해당 과목의 강의 콘텐츠에 게시됩니다. 강의 자료는 해당주의 수강 기간에만, 원격 강의 동영상은 기말 고사 전날까지만 공개됩니다.
원격 강의는 해당주의 월요일 13:00 부터 금요일 20:00 까지 수강 가능합니다. 해당 기간에 수강치 않으면 해당주의 수업은 모두 결석으로 처리됩니다. 필요시 유고 결석 신청하세요. 다만 첫 2주 강의는 수강 변경한 학생을 위해 9.20까지 수강이 가능합니다.
<성적 및 시험>
최종 성적은 기말고사(60%), 과제물(20%), 출석(20%)으로 정해집니다.
기말고사에 참석하지 않거나, 과제물을 모두 제출하지 않거나, 출석 일수 미달 시에는 학점이 부여되지 않습니다
기말고사는 15주차에 온라인으로 실시합니다. 시험 일시 및 범위는 추후 통보합니다. 기말고사는 다음에 설명할 과제물 제출과 같은 방법으로 이메일로 제출합니다.

## Slide 8: Notice(주의사항) - 2
<과제물 관련>
과제물은 총 4번 부여 됩니다. 과제물 제출은 해당 주의 일요일 20:00에 마감합니다. 마감 시간 이후에 제출되는 과제물은 0점으로 처리됩니다.
각 과제물은 답이 아닌 풀이 과정을 평가하여 3단계 (상, 중 하)로 점수화 합니다.
과제물을 부여한 다음주에 과제물에 대한 해설 원격 강의가 제공됩니다. 공정한 과제 평가를 위해 해설 강의 이전에 과제물 풀이에 대한 질문은 받지 않습니다.
과제물은 이메일(kscho@dankook.ac.kr)로 제출하며, 파일을 절대 첨부하지 말고 메일 본문에 직접(copy and paste는 안됩니다.) 과제에 대한 답을 적어야 합니다. 이메일의 제목은 반드시 “과제번호-분반-이름-학번”으로 해야 합니다 (예, 과제1-분반1-홍길동-1234567) 이를 지키지 않으면 감점이 됩니다. 과제번호는 각 과제부여시 표시됩니다.
<보강 관련>
월요일 또는 수요일이 공휴일(또는 대체 공휴일)인 10.4(월), 10.11(월), 11.3(수)에 대한 보강 수업은 해당 공휴일이 속한 주에 수행합니다.
다만, 해당 주의 월요일과 수요일이 모두 공휴일(또는 대체 공휴일) 인 9.20(월) 및 9.22(수)에 대한 보강은 학기말 보강일로 진행합니다.

## Slide 9: William Stallings Computer Organization and Architecture 10th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 10/e, by William Stallings, Chapter 1 “Introduction”.

## Slide 10: Chapter 1
Basic Concepts and Computer Evolution
Notes: In a class of computers called microcomputers, the relationship between architecture
and organization is very close. Changes in technology not only influence
organization but also result in the introduction of more powerful and more complex
architectures. Generally, there is less of a requirement for generation-
To-generation compatibility for these smaller machines. Thus, there is more interplay between
organizational and architectural design decisions. An intriguing example of this is
the reduced instruction set computer (RISC), which we examine in Chapter 15.
This book examines both computer organization and computer architecture.
The emphasis is perhaps more on the side of organization. However, because a
computer organization must be designed to implement a particular architectural
specification, a thorough treatment of organization requires a detailed examination
of architecture as well.

## Slide 11: Computer System
  Computer?
  Language (Program)
    Machine language, HLL, Natural Language
  Structure
    Thinking, Decision, Computation
    Memory(Storage)
    Action
Notes: Both the structure and functioning of a computer are, in essence, simple. Figure 1.1
depicts the basic functions that a computer can perform. In general terms, there are
only four:
Data Processing. The data may take a wide
variety of forms, and the range of processing requirements is broad. However, we
shall see that there are only a few fundamental methods or types of data processing.
Data Storage. Even if the computer is processing
data on the fly (i.e., data come in and get processed, and the results go out
immediately), the computer must temporarily store at least those pieces of data
that are being worked on at any given moment. Thus, there is at least a short-term
data storage function. Equally important, the computer performs a long-term data
storage function. Files of data are stored on the computer for subsequent retrieval
and update.
Data Movement. The computer’s operating environment consists of devices that serve as
either sources or destinations of data. When data are received from or delivered to
a device that is directly connected to the computer, the process is known as input–
output (I/O), and the device is referred to as a peripheral. When data are moved
over longer distances, to or from a remote device, the process is known as data
communications.
Control. Within the computer, a control unit manages the computer’s resources and orchestrates the
performance of its functional parts in response to those instructions.

## Slide 12: Structure
Notes: We now look in a general way at the internal structure of a computer. We begin with
a traditional computer with a single processor that employs a microprogrammed
control unit, then examine a typical multicore structure.
Figure 1.1 provides a hierarchical view
of the internal structure of a traditional single-processor computer.

## Slide 13
CPU – controls the operation of the computer and performs its data processing functions
Main Memory – stores data
I/O – moves data between the computer and its external environment
System Interconnection – some mechanism that provides for communication among CPU, main memory, and I/O
There are four main structural components
of the computer:
Notes: There are four main structural components:
• Central processing unit (CPU): Controls the operation of the computer and
performs its data processing functions; often simply referred to as processor.
• Main memory: Stores data.
• I/O: Moves data between the computer and its external environment.
• System interconnection: Some mechanism that provides for communication
among CPU, main memory, and I/O. A common example of system interconnection
is by means of a system bus, consisting of a number of conducting
wires to which all the other components attach.

## Slide 14: CPU
Control Unit
  Controls the operation of the CPU and hence the computer
  Arithmetic and Logic Unit (ALU)
  Performs the computer’s data processing function
  Registers
  Provide storage internal to the CPU
  CPU Interconnection
  Some mechanism that provides for communication among the control unit, ALU, and registers
Major structural components:
Notes: There may be one or more of each of the aforementioned components.
Traditionally, there has been just a single processor. In recent years, there has been
increasing use of multiple processors in a single computer. Some design issues relating
to multiple processors crop up and are discussed as the text proceeds; Part Five
focuses on such computers.
Each of these components will be examined in some detail in Part Two.
However, for our purposes, the most interesting and in some ways the most complex
component is the CPU. Its major structural components are as follows:
• Control unit: Controls the operation of the CPU and hence the computer.
• Arithmetic and logic unit (ALU): Performs the computer’s data processing
functions.
• Registers: Provides storage internal to the CPU.
• CPU interconnection: Some mechanism that provides for communication
among the control unit, ALU, and registers.
Part Three covers these components, where we will see that complexity is added by
the use of parallel and pipelined organizational techniques. Finally, there are several
approaches to the implementation of the control unit; one common approach is
a microprogrammed implementation. In essence, a microprogrammed control unit
operates by executing microinstructions that define the functionality of the control
unit. With this approach, the structure of the control unit can be depicted, as in
Figure 1.1. This structure is examined in Part Four.

## Slide 15: Multicore Computer Structure
Central processing unit (CPU)
  Portion of the computer that fetches and executes instructions
  Consists of an ALU, a control unit, and registers
  Referred to as a processor in a system with a single processing unit
Core
  An individual processing unit on a processor chip
  May be equivalent in functionality to a CPU on a single-CPU system
  Specialized processing units are also referred to as cores
Processor
  A physical piece of silicon containing one or more cores
  Is the computer component that interprets and executes instructions
  Referred to as a multicore processor if it contains multiple cores
Notes: As was mentioned, contemporary
computers generally have multiple processors. When these processors all reside
on a single chip, the term multicore computer is used, and each processing unit
(consisting of a control unit, ALU, registers, and perhaps cache) is called a core . To
clarify the terminology, this text will use the following definitions.
■ Central processing unit (CPU) : That portion of a computer that fetches and
executes instructions. It consists of an ALU, a control unit, and registers. In a
system with a single processing unit, it is often simply referred to as a processor .
■ Core : An individual processing unit on a processor chip. A core may be
equivalent in functionality to a CPU on a single-CPU system. Other specialized processing units,
such as one optimized for vector and matrix operations, are also referred to as cores.
■ Processor: A physical piece of silicon containing one or more cores. The
processor is the computer component that interprets and executes instructions.
If a processor contains multiple cores, it is referred to as a multicore
processor .
After about a decade of discussion, there is broad industry consensus on this
usage.

## Slide 16: Cache Memory
Multiple layers of memory between the processor and main memory
Is smaller and faster than main memory
Used to speed up memory access by placing in the cache data from main memory that is likely to be used in the near future
A greater performance improvement may be obtained by using multiple levels of cache, with level 1 (L1) closest to the core and additional levels (L2, L3, etc.) progressively farther from the core (???)
Notes: Another prominent feature of contemporary computers is the use of multiple
layers of memory, called cache memory , between the processor and main memory.
Chapter 4 is devoted to the topic of cache memory. For our purposes in this section,
we simply note that a cache memory is smaller and faster than main memory and is
used to speed up memory access by placing in the cache, data from main memory
that is likely to be used in the near future. A greater performance improvement may
be obtained by using multiple levels of cache, with level 1 (L1) closest to the core
and additional levels (L2, L3, and so on) progressively farther from the core. In this
scheme, level n is smaller and faster than level n + 1.

## Slide 17
Notes: Figure 1.2 is a simplified view of the principal components of a typical multicore
computer. Most computers, including embedded computers in smartphones
and tablets, plus personal computers, laptops, and workstations, are housed on a
motherboard. Before describing this arrangement, we need to define some terms.
A printed circuit board is a rigid, flat board that holds and interconnects chips and
other electronic components. The board is made of layers, typically two to ten,
that interconnect components via copper pathways that are etched into the board.
The main printed circuit board (PCB) in a computer is called a system board or
motherboard , while smaller ones that plug into the slots in the main board are
called expansion boards.
The most prominent elements on the motherboard are the chips. A chip is
a single piece of semiconducting material, typically silicon, upon which electronic
circuits and logic gates are fabricated. The resulting product is referred to as an
integrated circuit .
The motherboard contains a slot or socket for the processor chip, which typically
contains multiple individual cores, in what is known as a multicore processor .
There are also slots for memory chips, I/O controller chips, and other key computer
components. For desktop computers, expansion slots enable the inclusion of more
components on expansion boards. Thus, a modern motherboard connects only a
few individual chip components, with each chip containing from a few thousand up
to hundreds of millions of transistors.
Figure 1.2 shows a processor chip that contains eight cores and an L3 cache.
Not shown is the logic required to control operations between the cores and the
cache and between the cores and the external circuitry on the motherboard. The
figure indicates that the L3 cache occupies two distinct portions of the chip surface.
However, typically, all cores have access to the entire L3 cache via the aforementioned
control circuits. The processor chip shown in Figure 1.2 does not represent
any specific product, but provides a general idea of how such chips are laid out.
Next, we zoom in on the structure of a single core, which occupies a portion of
the processor chip. In general terms, the functional elements of a core are:
■ Instruction logic: This includes the tasks involved in fetching instructions and
decoding each instruction to determine the instruction operation and the
memory locations of any operands.
■ Arithmetic and logic unit (ALU): Performs the operation specified by an
instruction.
■ Load/store logic: Manages the transfer of data to and from main memory via
cache.
The core also contains an L1 cache, split between an instruction cache
(I-cache) that is used for the transfer of instructions to and from main memory, and
an L1 data cache, for the transfer of operands and results. Typically, today’s processor
chips also include an L2 cache as part of the core. In many cases, this cache
is also split between instruction and data caches, although a combined, single L2
cache is also used.
Keep in mind that this representation of the layout of the core is only intended
to give a general idea of internal core structure. In a given product, the functional
elements may not be laid out as the three distinct elements shown in Figure 1.2,
especially if some or all of these functions are implemented as part of a microprogrammed
control unit.

## Slide 18
Figure 1.3
Motherboard with Two Intel Quad-Core Xeon Processors
Notes: It will be instructive to look at some real-
world examples that illustrate the hierarchical structure of computers.
Figure 1.3 is a photograph of the
motherboard for a computer built around two Intel Quad-Core
Xeon processor chips. Many of the elements labeled on the photograph are discussed subsequently
in this book. Here, we mention the most important, in addition to the processor
sockets:
■ PCI-Express slots for a high-end
display adapter and for additional peripherals
(Section 3.6 describes PCIe).
■ Ethernet controller and Ethernet ports for network connections.
■ USB sockets for peripheral devices.
■ Serial ATA (SATA) sockets for connection to disk memory (Section 7.7
discusses Ethernet, USB, and SATA).
■ Interfaces for DDR (double data rate) main memory chips (Section 5.3
discusses DDR).
■ Intel 3420 chipset is an I/O controller for direct memory access operations
between peripheral devices and main memory (Section 7.5 discusses DDR).

## Slide 19: Computer
  Architecture vs. Program
  HLL => machine language
  Performance (System)
    Time
    Throughput
  CPU vs. Memory
    Ex)
Notes: Both the structure and functioning of a computer are, in essence, simple. Figure 1.1
depicts the basic functions that a computer can perform. In general terms, there are
only four:
Data Processing. The data may take a wide
variety of forms, and the range of processing requirements is broad. However, we
shall see that there are only a few fundamental methods or types of data processing.
Data Storage. Even if the computer is processing
data on the fly (i.e., data come in and get processed, and the results go out
immediately), the computer must temporarily store at least those pieces of data
that are being worked on at any given moment. Thus, there is at least a short-term
data storage function. Equally important, the computer performs a long-term data
storage function. Files of data are stored on the computer for subsequent retrieval
and update.
Data Movement. The computer’s operating environment consists of devices that serve as
either sources or destinations of data. When data are received from or delivered to
a device that is directly connected to the computer, the process is known as input–
output (I/O), and the device is referred to as a peripheral. When data are moved
over longer distances, to or from a remote device, the process is known as data
communications.
Control. Within the computer, a control unit manages the computer’s resources and orchestrates the
performance of its functional parts in response to those instructions.

## Slide 20: Table 1.2 Computer Generations
Notes: It has become widely accepted to classify computers into generations based on the fundamental
hardware technology employed (Table 1.2). Each new generation is characterized
by greater processing performance, larger memory capacity, and smaller
size than the previous one.

## Slide 21: History of Computers
Vacuum tubes were used for digital logic elements and memory
IAS computer
  Fundamental design approach was the stored program concept
    Attributed to the mathematician John von Neumann
    First publication of the idea was in 1945 for the EDVAC
  Design began at the Princeton Institute for Advanced Studies
  Completed in 1952
  Prototype of all subsequent general-purpose computers
First Generation: Vacuum Tubes
Notes: The first generation of computers used vacuum tubes for digital logic elements and
memory. A number of research and then commercial computers were built using
vacuum tubes. For our purposes, it will be instructive to examine perhaps the most
famous first-generation computer, known as the IAS computer.
A fundamental design approach first implemented in the IAS computer is
known as the stored-program concept . This idea is usually attributed to the mathematician
John von Neumann. Alan Turing developed the idea at about the same time.
The first publication of the idea was in a 1945 proposal by von Neumann for a new
computer, the EDVAC (Electronic Discrete Variable Computer).3
In 1946, von Neumann and his colleagues began the design of a new stored-
program computer, referred to as the IAS computer, at the Princeton Institute for
Advanced Studies. The IAS computer, although not completed until 1952, is the
prototype of all subsequent general-purpose computers.

## Slide 22
Notes: Figure 1.6 shows the general structure of the IAS computer (compare with Figure 1.1).
It consists of
• A main memory, which stores both data and instructions
• An arithmetic and logic unit (ALU) capable of operating on binary data
• A control unit, which interprets the instructions in memory and causes them
to be executed
• Input/output (I/O) equipment operated by the control unit
This structure was outlined in von Neumann’s earlier proposal, which is worth
quoting in part at this point [VONN45]:
2.2 First: Since the device is primarily a computer, it will
have to perform the elementary operations of arithmetic most frequently.
These are addition, subtraction, multiplication, and division.
It is therefore reasonable that it should contain specialized
organs for just these operations.
It must be observed, however, that while this principle as such
is probably sound, the specific way in which it is realized requires
close scrutiny. At any rate a central arithmetical part of the device will
probably have to exist, and this constitutes the first specific part: CA .
2.3 Second: The logical control of the device, that is, the
proper sequencing of its operations, can be most efficiently carried
out by a central control organ. If the device is to be elastic ,
that is, as nearly as possible all purpose , then a distinction must
be made between the specific instructions given for and defining
a particular problem, and the general control organs that see to it
that these instructions—no matter what they are—are
carried out. The former must be stored in some way; the latter are represented
by definite operating parts of the device. By the central control we
mean this latter function only, and the organs that perform it form
the second specific part: CC .
2.4 Third: Any device that is to carry out long and complicated
sequences of operations (specifically of calculations) must
have a considerable memory . . .
The instructions which govern a complicated problem may
constitute considerable material, particularly so, if the code is circumstantial
(which it is in most arrangements). This material must
be remembered.
At any rate, the total memory constitutes the third specific
part of the device: M.
2.6 The three specific parts CA, CC (together C), and M correspond
to the associative neurons in the human nervous system. It
remains to discuss the equivalents of the sensory or afferent and the
motor or efferent neurons. These are the input and output organs of
the device. The device must be endowed with the ability to maintain
input and output (sensory and motor) contact with some specific
medium of this type. The medium will be called the outside recording
medium of the device: R .
2.7 Fourth: The device must have organs to transfer information
from R into its specific parts C and M. These organs form its
input , the fourth specific part: I . It will be seen that it is best to make
all transfers from R (by I) into M and never directly from C.
2.8 Fifth: The device must have organs to transfer from its
specific parts C and M into R. These organs form its output , the
fifth specific part: O . It will be seen that it is again best to make all
transfers from M (by O) into R, and never directly from C.

## Slide 23
Notes: With rare exceptions, all of today’s computers have this same general structure
and function and are thus referred to as von Neumann machines . Thus, it is worthwhile
at this point to describe briefly the operation of the IAS computer [BURK46,
GOLD54]. Following [HAYE98], the terminology and notation of von Neumann
are changed in the following to conform more closely to modern usage; the examples
accompanying this discussion are based on that latter text.
The memory of the IAS consists of 4,096 storage locations, called words , of
40 binary digits (bits) each.6 Both data and instructions are stored there. Numbers are
represented in binary form, and each instruction is a binary code. Figure 1.7 illustrates
these formats. Each number is represented by a sign bit and a 39-bit value. A word
may alternatively contain two 20-bit instructions, with each instruction consisting
of an 8-bit operation code (opcode ) specifying the operation to be performed and
a 12-bit address designating one of the words in memory (numbered from 0 to 999).

## Slide 24: Registers
Memory buffer register (MBR)
Contains a word to be stored in memory or sent to the I/O unit
Or is used to receive a word from memory or from the I/O unit
Memory address register (MAR)
Specifies the address in memory of the word to be written from or read into the MBR
Instruction register (IR)
Contains the 8-bit opcode instruction being executed
Instruction buffer register (IBR)
Employed to temporarily hold the right-hand instruction from a word in memory
Program counter (PC)
Contains the address of the next instruction pair to be fetched from memory
Accumulator (AC) and multiplier quotient (MQ)
Employed to temporarily hold operands and results of ALU operations
Notes: The control unit operates the IAS by fetching instructions from memory
and executing them one at a time. We explain these operations with reference to
Figure 1.6. This figure reveals that both the control unit and the ALU contain storage
locations, called registers , defined as follows:
Memory buffer register (MBR): Contains a word to be stored in memory or sent
to the I/O unit, or is used to receive a word from memory or from the I/O unit.
• Memory address register (MAR): Specifies the address in memory of the word
to be written from or read into the MBR.
• Instruction register (IR ): Contains the 8-bit opcode instruction being executed.
• Instruction buffer register (IBR): Employed to hold temporarily the right-hand
instruction from a word in memory.
• Program counter (PC): Contains the address of the next instruction pair to be
fetched from memory.
• Accumulator (AC) and multiplier quotient (MQ): Employed to hold temporarily
operands and results of ALU operations. For example, the result of
multiplying two 40-bit numbers is an 80-bit number; the most significant 40 bits
are stored in the AC and the least significant in the MQ.

## Slide 25: History of Computers
  Smaller
  Cheaper
  Dissipates less heat than a vacuum tube
  Is a solid state device made from silicon
  Was invented at Bell Labs in 1947
  It was not until the late 1950’s that fully transistorized computers were commercially available
Second Generation: Transistors
Notes: The first major change in the electronic computer came with the replacement of
the vacuum tube by the transistor. The transistor is smaller, cheaper, and dissipates
less heat than a vacuum tube but can be used in the same way as a vacuum tube to
construct computers. Unlike the vacuum tube, which requires wires, metal plates, a
glass capsule, and a vacuum, the transistor is a solid-state device, made from silicon.
The transistor was invented at Bell Labs in 1947 and by the 1950s had launched
an electronic revolution. It was not until the late 1950s, however, that fully transistorized
computers were commercially available. The use of the transistor defines
the second generation of computers.

## Slide 26: Second Generation Computers
Introduced:
  More complex arithmetic and logic units and control units
  The use of high-level programming languages
  Provision of system software which provided the ability to:
    Load programs
    Move data to peripherals
    Libraries perform common computations
Notes: But there are other changes as well. The second generation saw the introduction
of more complex arithmetic and logic units and control units, the use of
high-level programming languages, and the provision of system software with the
computer. In broad terms, system software provided the ability to load programs,
move data to peripherals, and libraries to perform common computations, similar
to what modern operating systems like Windows and Linux do.

## Slide 27
Notes: It will be useful to examine an important member of the second generation: the
IBM 7094 [BELL71]. From the introduction of the 700 series in 1952 to the introduction
of the last member of the 7000 series in 1964, this IBM product line underwent
an evolution that is typical of computer products. Successive members of the product
line showed increased performance, increased capacity, and/or lower cost.
Also, over the lifetime of this series of computers, the relative speed of the
CPU increased by a factor of 50. Speed improvements are achieved by improved
electronics (e.g., a transistor implementation is faster than a vacuum tube implementation)
and more complex circuitry. For example, the IBM 7094 includes an
Instruction Backup Register, used to buffer the next instruction. The control unit
fetches two adjacent words from memory for an instruction fetch. Except for the
occurrence of a branching instruction, which is relatively infrequent (perhaps 10 to
15%), this means that the control unit has to access memory for an instruction on
only half the instruction cycles. This prefetching significantly reduces the average
instruction cycle time.
Figure 1.9 shows a large (many peripherals) configuration for an IBM 7094,
which is representative of second-generation computers. Several differences from
the IAS computer are worth noting. The most important of these is the use of data
channels . A data channel is an independent I/O module with its own processor and
instruction set. In a computer system with such devices, the CPU does not execute
detailed I/O instructions. Such instructions are stored in a main memory to be
executed by a special-purpose processor in the data channel itself. The CPU initiates
an I/O transfer by sending a control signal to the data channel, instructing it to
execute a sequence of instructions in memory. The data channel performs its task
independently of the CPU and signals the CPU when the operation is complete.
This arrangement relieves the CPU of a considerable processing burden.
Another new feature is the multiplexor , which is the central termination
point for data channels, the CPU, and memory. The multiplexor schedules access
to the memory from the CPU and data channels, allowing these devices to act
independently.

## Slide 28: History of Computers
Third Generation: Integrated Circuits
1958 – the invention of the integrated circuit
Discrete component
  Single, self-contained transistor
  Manufactured separately, packaged in their own containers, and soldered or wired together onto masonite-like circuit boards
  Manufacturing process was expensive and cumbersome
  The two most important members of the third generation were the IBM System/360 and the DEC PDP-8
Notes: A single, self-contained transistor is called a discrete component. Throughout the
1950s and early 1960s, electronic equipment was composed largely of discrete components—
transistors, resistors, capacitors, and so on. Discrete components were
manufactured separately, packaged in their own containers, and soldered or wired
together onto masonite-like circuit boards, which were then installed in computers,
oscilloscopes, and other electronic equipment. Whenever an electronic device called
for a transistor, a little tube of metal containing a pinhead-sized piece of silicon
had to be soldered to a circuit board. The entire manufacturing process, from transistor
to circuit board, was expensive and cumbersome.
These facts of life were beginning to create problems in the computer industry.
Early second-generation computers contained about 10,000 transistors. This
figure grew to the hundreds of thousands, making the manufacture of newer, more
powerful machines increasingly difficult.
In 1958 came the achievement that revolutionized electronics and started the
era of microelectronics: the invention of the integrated circuit. It is the integrated
circuit that defines the third generation of computers. In this section, we provide a
brief introduction to the technology of integrated circuits. Then we look at perhaps
the two most important members of the third generation, both of which were introduced
at the beginning of that era: the IBM System/360 and the DEC PDP-8.

## Slide 29
Notes: Microelectronics means, literally, “small electronics.” Since
the beginnings of digital electronics and the computer industry, there has been a
persistent and consistent trend toward the reduction in size of digital electronic
circuits. Before examining the implications and benefits of this trend, we need to
say something about the nature of digital electronics. A more detailed discussion is
found in Chapter 11.
The basic elements of a digital computer, as we know, must perform storage,
movement, processing, and control functions. Only two fundamental types of components
are required (Figure 1.10): gates and memory cells. A gate is a device that
implements a simple Boolean or logical function, such as IF A AND B ARE TRUE
THEN C IS TRUE (AND gate). Such devices are called gates because they control
data flow in much the same way that canal gates control the flow of water. The
memory cell is a device that can store one bit of data; that is, the device can be in
one of two stable states at any time. By interconnecting large numbers of these
fundamental devices, we can construct a computer.

## Slide 30: Integrated Circuits
A computer consists of gates, memory cells, and interconnections among these elements
The gates and memory cells are constructed of simple digital electronic components
Data storage – provided by memory cells
Data processing – provided by gates
Data movement – the paths among components are used to move data from memory to memory and from memory through gates to memory
Control – the paths among components can carry control signals
Exploits the fact that such components as transistors, resistors, and conductors can be fabricated from a semiconductor such as silicon
Many transistors can be produced at the same time on a single wafer of silicon
Transistors can be connected with a processor metallization to form circuits
Notes: We can relate this to our four
basic functions as follows:
• Data storage: Provided by memory cells.
• Data processing: Provided by gates.
• Data movement: The paths among components are used to move data from
memory to memory and from memory through gates to memory.
• Control: The paths among components can carry control signals. For example,
a gate will have one or two data inputs plus a control signal input that activates
the gate. When the control signal is ON, the gate performs its function on the
data inputs and produces a data output. Similarly, the memory cell will store
the bit that is on its input lead when the WRITE control signal is ON and will
place the bit that is in the cell on its output lead when the READ control signal
is ON.
Thus, a computer consists of gates, memory cells, and interconnections among these
elements. The gates and memory cells are, in turn, constructed of simple digital
electronic components.
The integrated circuit exploits the fact that such components as transistors,
resistors, and conductors can be fabricated from a semiconductor such as silicon.
It is merely an extension of the solid-state art to fabricate an entire circuit in a tiny
piece of silicon rather than assemble discrete components made from separate
pieces of silicon into the same circuit. Many transistors can be produced at the same
time on a single wafer of silicon. Equally important, these transistors can be connected
with a process of metallization to form circuits.

## Slide 31
Notes: Figure 1.11 depicts the key concepts in an integrated circuit. A thin wafer of
silicon is divided into a matrix of small areas, each a few millimeters square. The
identical circuit pattern is fabricated in each area, and the wafer is broken up into
chips. Each chip consists of many gates and/or memory cells plus a number of input
and output attachment points. This chip is then packaged in housing that protects
it and provides pins for attachment to devices beyond the chip. A number of these
packages can then be interconnected on a printed circuit board to produce larger
and more complex circuits.

## Slide 32
Notes: Initially, only a few gates or memory cells could be reliably manufactured
and packaged together. These early integrated circuits are referred to as small scale
Integration (SSI). As time went on, it became possible to pack more and more
Components on the same chip. This growth in density is illustrated in Figure 1.12; it is
one of the most remarkable technological trends ever recorded.
This figure reflects the
famous Moore’s law, which was propounded by Gordon Moore, cofounder of Intel,
in 1965 [MOOR65]. Moore observed that the number of transistors that could be
put on a single chip was doubling every year and correctly predicted that this pace
would continue into the near future. To the surprise of many, including Moore, the
pace continued year after year and decade after decade. The pace slowed to a doubling
every 18 months in the 1970s but has sustained that rate ever since.

## Slide 33: Moore’s Law
1965; Gordon Moore – co-founder of Intel
Observed number of transistors that could be put on a single chip was doubling every year
The pace slowed to a doubling every 18 months in the 1970’s but has sustained that rate ever since
Consequences of Moore’s law:
The cost of computer logic and memory circuitry has fallen at a dramatic rate
The electrical path length is shortened, increasing operating speed
Computer becomes smaller and is more convenient to use in a variety of environments
Reduction in power and cooling requirements
Fewer interchip connections
Notes: The consequences of Moore’s law are profound:
1. The cost of a chip has remained virtually unchanged during this period of
rapid growth in density. This means that the cost of computer logic and memory
circuitry has fallen at a dramatic rate.
2. Because logic and memory elements are placed closer together on more
densely packed chips, the electrical path length is shortened, increasing
operating speed.
3. The computer becomes smaller, making it more convenient to place in a
variety of environments.
4. There is a reduction in power and cooling requirements.
5. The interconnections on the integrated circuit are much more reliable than
solder connections. With more circuitry on each chip, there are fewer interchip
connections.

## Slide 34: IBM System/360
Announced in 1964
Product line was incompatible with older IBM machines
Was the success of the decade and cemented IBM as the overwhelmingly dominant computer vendor
The architecture remains to this day the architecture of IBM’s mainframe computers
Was the industry’s first planned family of computers
  Models were compatible in the sense that a program written for one model should be capable of being executed by another model in the series
Notes: By 1964, IBM had a firm grip on the computer market with
its 7000 series of machines. In that year, IBM announced the System/360, a new
family of computer products. Although the announcement itself was no surprise, it
contained some unpleasant news for current IBM customers: the 360 product line
was incompatible with older IBM machines. Thus, the transition to the 360 would be
difficult for the current customer base. This was a bold step by IBM, but one IBM felt
was necessary to break out of some of the constraints of the 7000 architecture and
to produce a system capable of evolving with the new integrated circuit technology
[PADE81, GIFF87]. The strategy paid off both financially and technically. The 360
was the success of the decade and cemented IBM as the overwhelmingly dominant
computer vendor, with a market share above 70%. And, with some modifications
and extensions, the architecture of the 360 remains to this day the architecture
of IBM’s mainframe computers. Examples using this architecture can be found
throughout this text.
The System/360 was the industry’s first planned family of computers. The
family covered a wide range of performance and cost. The models were compatible in the sense that
a program written for one model should be capable of being executed by another
model in the series, with only a difference in the time it takes to execute.

## Slide 35: Family Characteristics
Similar or identical instruction set
Similar or identical operating system
Increasing speed
Increasing number of I/O ports
Increasing memory size
Increasing cost
Notes: The concept of a family of compatible computers was both novel and
extremely successful. A customer with modest requirements and a budget to match
could start with the relatively inexpensive Model 30. Later, if the customer’s needs
grew, it was possible to upgrade to a faster machine with more memory without
sacrificing the investment in already-developed software. The characteristics of a
family are as follows:
• Similar or identical instruction set: In many cases, the exact same set of machine
instructions is supported on all members of the family. Thus, a program that
executes on one machine will also execute on any other. In some cases, the
lower end of the family has an instruction set that is a subset of that of the top
end of the family. This means that programs can move up but not down.
• Similar or identical operating system: The same basic operating system is
available for all family members. In some cases, additional features are added
to the higher-end members.
• Increasing speed: The rate of instruction execution increases in going from
lower to higher family members.
• Increasing number of I /O ports: The number of I/O ports increases in going
from lower to higher family members.
• Increasing memory size: The size of main memory increases in going from
lower to higher family members.
• Increasing cost: At a given point in time, the cost of a system increases in going
from lower to higher family members.
How could such a family concept be implemented? Differences were achieved
based on three factors: basic speed, size, and degree of simultaneity [STEV64]. For
example, greater speed in the execution of a given instruction could be gained by
the use of more complex circuitry in the ALU, allowing suboperations to be carried
out in parallel. Another way of increasing speed was to increase the width of the
data path between main memory and the CPU. On the Model 30, only 1 byte (8 bits)
could be fetched from main memory at a time, whereas 8 bytes could be fetched at
a time on the Model 75.
The System/360 not only dictated the future course of IBM but also had a
profound impact on the entire industry. Many of its features have become standard on
other large computers.

## Slide 36
Notes: In the same year that IBM shipped its first System/360, another
momentous first shipment occurred: PDP-8
from Digital Equipment Corporation(DEC). At a time when the average
computer required an air-conditioned room, the PDP-8
(dubbed a minicomputer by the industry, after the miniskirt of the day)
was small enough that it could be placed on top of a lab bench or be built into
other equipment. It could not do everything the mainframe could, but at $16,000, it
was cheap enough for each lab technician to have one. In contrast, the System/360
series of mainframe computers introduced just a few months before cost hundreds
of thousands of dollars.
The low cost and small size of the PDP-8
enabled another manufacturer to purchase a PDP-8
and integrate it into a total system for resale. These other manufacturers
came to be known as original equipment manufacturers (OEMs) , and the
OEM market became and remains a major segment of the computer marketplace.
In contrast to the central-switched architecture (Figure 1.9) used by IBM on its
700/7000 and 360 systems, later models of the PDP-8
used a structure that became virtually
universal for microcomputers: the bus structure. This is illustrated in Figure 1.13.
The PDP-8 bus, called the Omnibus, consists of 96 separate signal paths, used to carry
control, address, and data signals. Because all system components share a common
set of signal paths, their use can be controlled by the CPU. This architecture is highly
flexible, allowing modules to be plugged into the bus to create various configurations.
It is only in recent years that the bus structure has given way to a structure known as
Point-to-point interconnect, described in Chapter 3.

## Slide 37: Semiconductor Memory Microprocessors
Later
Generations
LSI
Large
Scale Integration
VLSI
Very Large Scale Integration
ULSI
Ultra Large
Scale
Integration
Notes: Beyond the third generation there is less general agreement on defining generations
of computers. Table 1.2 suggests that there have been a number of later generations,
based on advances in integrated circuit technology. With the introduction
of large-scale integration (LSI), more than 1000 components can be placed on a
single integrated circuit chip. Very-large-scale integration (VLSI) achieved more
than 10,000 components per chip, while current ultra-large-scale integration (ULSI)
chips can contain more than one billion components.
With the rapid pace of technology, the high rate of introduction of new products,
and the importance of software and communications as well as hardware, the
classification by generation becomes less clear and less meaningful. In this section,
we mention two of the most important of developments in later generations.

## Slide 38: Microprocessors
The density of elements on processor chips continued to rise
  More and more elements were placed on each chip so that fewer and fewer chips were needed to construct a single computer processor
1971 Intel developed 4004
  First chip to contain all of the components of a CPU on a single chip
  Birth of microprocessor
1972 Intel developed 8008
  First 8-bit microprocessor
1974 Intel developed 8080
  First general purpose microprocessor
  Faster, has a richer instruction set, has a large addressing capability
Notes: Just as the density of elements on memory chips has continued
to rise, so has the density of elements on processor chips. As time went on, more
and more elements were placed on each chip, so that fewer and fewer chips were
needed to construct a single computer processor.
A breakthrough was achieved in 1971, when Intel developed its 4004. The
4004 was the first chip to contain all of the components of a CPU on a single chip:
The microprocessor was born.
The 4004 can add two 4-bit numbers and can multiply only by repeated addition.
By today’s standards, the 4004 is hopelessly primitive, but it marked the beginning of
a continuing evolution of microprocessor capability and power.
This evolution can be seen most easily in the number of bits that the processor
deals with at a time. There is no clear-cut measure of this, but perhaps the best measure
is the data bus width: the number of bits of data that can be brought into or sent
out of the processor at a time. Another measure is the number of bits in the accumulator
or in the set of general-purpose registers. Often, these measures coincide, but
not always. For example, a number of microprocessors were developed that operate
on 16-bit numbers in registers but can only read and write 8 bits at a time.
The next major step in the evolution of the microprocessor was the introduction
in 1972 of the Intel 8008. This was the first 8-bit microprocessor and was almost twice
as complex as the 4004.
Neither of these steps was to have the impact of the next major event: the introduction
in 1974 of the Intel 8080. This was the first general-purpose microprocessor.
Whereas the 4004 and the 8008 had been designed for specific applications, the 8080
was designed to be the CPU of a general-purpose microcomputer. Like the 8008, the
8080 is an 8-bit microprocessor. The 8080, however, is faster, has a richer instruction
set, and has a large addressing capability.

## Slide 39: The Evolution of the Intel x86 Architecture
Two processor families are the Intel x86 and the ARM architectures
Current x86 offerings represent the results of decades of design effort on complex instruction set computers (CISCs)
An alternative approach to processor design is the reduced instruction set computer (RISC)
ARM architecture is used in a wide variety of embedded systems and is one of the most powerful and best-designed RISC-based systems on the market
Notes: Throughout this book, we rely on many concrete examples of computer design and
implementation to illustrate concepts and to illuminate trade-
offs. Numerous systems, both contemporary and historical, provide examples of important computer
architecture design features. But the book relies principally on examples from two
processor families: the Intel x86 and the ARM architectures. The current x86 offerings
represent the results of decades of design effort on complex instruction set
computers (CISCs). The x86 incorporates the sophisticated design principles once
found only on mainframes and supercomputers and serves as an excellent example
of CISC design. An alternative approach to processor design is the reduced instruction
set computer (RISC). The ARM architecture is used in a wide variety of embedded
systems and is one of the most powerful and best-
designed RISC-based systems
on the market. In this section and the next, we provide a brief overview of these two
systems.
In terms of market share, Intel has ranked as the number one maker of microprocessors
for non-embedded systems for decades, a position it seems unlikely to
yield. The evolution of its flagship microprocessor product serves as a good indicator
of the evolution of computer technology in general.
Table 1.3 shows that evolution. Interestingly, as microprocessors have grown
faster and much more complex, Intel has actually picked up the pace. Intel used
to develop microprocessors one after another, every four years. But Intel hopes
to keep rivals at bay by trimming a year or two off this development time, and has
done so with the most recent x86 generations.

## Slide 40: Highlights of the Evolution of the Intel Product Line:
8080
World’s first general-purpose microprocessor
8-bit machine, 8-bit data path to memory
Was used in the first personal computer (Altair)
8086
A more powerful 16-bit machine
Has an instruction cache, or queue, that prefetches a few instructions before they are executed
The first appearance of the x86 architecture
The 8088 was a variant of this processor and used in IBM’s first personal computer (securing the success of Intel
80286
Extension of the 8086 enabling addressing a 16-MB memory instead of just 1MB
80386
Intel’s first 32-bit machine
First Intel processor to support multitasking
80486
Introduced the use of much more sophisticated and powerful cache technology and sophisticated instruction pipelining
Also offered a built-in math coprocessor
Notes: It is worthwhile to list some of the highlights of the evolution of the Intel product
line:
■ 8080: The world’s first general-
purpose microprocessor. This was an 8-bit
machine, with an 8-bit data path to memory. The 8080 was used in the first
personal computer, the Altair.
■ 8086: A far more powerful, 16-bit machine. In addition to a wider data path
and larger registers, the 8086 sported an instruction cache, or queue, that
prefetches a few instructions before they are executed. A variant of this processor,
the 8088, was used in IBM’s first personal computer, securing the success
of Intel. The 8086 is the first appearance of the x86 architecture.
■ 80286: This extension of the 8086 enabled addressing a 16-MB memory instead
of just 1 MB.
■ 80386: Intel’s first 32-bit machine, and a major overhaul of the product. With
a 32-bit architecture, the 80386 rivaled the complexity and power of minicomputers
and mainframes introduced just a few years earlier. This was the first
Intel processor to support multitasking, meaning it could run multiple programs
at the same time.
■ 80486: The 80486 introduced the use of much more sophisticated and powerful
cache technology and sophisticated instruction pipelining. The 80486 also
offered a built-in math coprocessor, offloading complex math operations from
the main CPU.

## Slide 41: Highlights of the Evolution of the Intel Product Line:
Pentium
Pentium Pro
Pentium II
Pentium III
Pentium 4
Core
Core 2
Intel introduced the use of superscalar techniques, which allow multiple instructions to execute in parallel
Continued the move into superscalar organization with aggressive use of register renaming, branch prediction, data flow analysis, and speculative execution
Incorporated Intel MMX technology, which is designed specifically to process video, audio, and graphics data efficiently
Incorporated additional floating-point instructions
Streaming SIMD Extensions (SSE)
Includes additional floating-point and other enhancements for multimedia
First Intel x86 micro-core
Extends the Core architecture to 64 bits
Core 2 Quad provides four cores on a single chip
More recent Core offerings have up to 10 cores per chip
An important addition to the architecture was the Advanced Vector Extensions instruction set
Notes: ■ Pentium: With the Pentium, Intel introduced the use of superscalar techniques,
which allow multiple instructions to execute in parallel.
■ Pentium Pro: The Pentium Pro continued the move into superscalar organization
begun with the Pentium, with aggressive use of register renaming, branch
prediction, data flow analysis, and speculative execution.
■ Pentium II: The Pentium II incorporated Intel MMX technology, which is
designed specifically to process video, audio, and graphics data efficiently.
■ Pentium III: The Pentium III incorporates additional floating-
point instructions: The Streaming SIMD Extensions (SSE) instruction set extension added
70 new instructions designed to increase performance when exactly the same
operations are to be performed on multiple data objects. Typical applications
are digital signal processing and graphics processing.
■ Pentium 4: The Pentium 4 includes additional floating-
point and other enhancements for multimedia.
■ Core: This is the first Intel x86 microprocessor with a dual core, referring to
the implementation of two cores on a single chip.
■ Core 2: The Core 2 extends the Core architecture to 64 bits. The Core 2 Quad
provides four cores on a single chip. More recent Core offerings have up to 10
cores per chip. An important addition to the architecture was the Advanced
Vector Extensions instruction set that provided a set of 256-bit, and then 512-
bit, instructions for efficient processing of vector data.
Almost 40 years after its introduction in 1978, the x86 architecture continues to
dominate the processor market outside of embedded systems. Although the organization
and technology of the x86 machines have changed dramatically over the decades,
the instruction set architecture has evolved to remain backward compatible with earlier
versions. Thus, any program written on an older version of the x86 architecture
can execute on newer versions. All changes to the instruction set architecture have
involved additions to the instruction set, with no subtractions. The rate of change has
been the addition of roughly one instruction per month added to the architecture
[ANTH08], so that there are now thousands of instructions in the instruction set.
The x86 provides an excellent illustration of the advances in computer hardware
over the past 35 years. The 1978 8086 was introduced with a clock speed of
5 MHz and had 29,000 transistors. A six-
core Core i7 EE 4960X introduced in 2013
operates at 4 GHz, a speedup of a factor of 800, and has 1.86 billion transistors,
about 64,000 times as many as the 8086. Yet the Core i7 EE 4960X is in only a
slightly larger package than the 8086 and has a comparable cost.

## Slide 42: Summary
Organization and architecture
Structure and function
Brief history of computers
  The First Generation: Vacuum tubes
  The Second Generation: Transistors
  The Third Generation: Integrated Circuits
  Later generations
  The evolution of the Intel x86 architecture
  Cloud computing
  Basic concepts
  Cloud services
Embedded systems
  The Internet of things
  Embedded operating systems
  Application processors versus dedicated processors
  Microprocessors versus microcontrollers
  Embedded versus deeply embedded systems
ARM architecture
  ARM evolution
  Instruction set architecture
  ARM products
Chapter 1
Basic Concepts and Computer Evolution
Notes: Chapter 1 summary.